## Slide 1: EPA’s Ozone Advance Program
What Participation Could Mean for Shreveport –Bossier and NW Louisiana Area

## Slide 2: Presentation Overview
Ozone Basics
What is the attainment outlook for this area?
Why should attainment areas work to reduce ozone?
Who can participate?
What are the criteria for program eligibility?
What might you get out of participating?
What does participation mean?

## Slide 3: What is Ozone ?
Ozone is commonly referred to as smog.
It is not emitted, but forms in the atmosphere under certain conditions
Volatile Organic Compounds (VOC) + Nitrogen Oxides (NOx) + Sunlight = Ozone
In other words, emissions from business and industry + cars + sunshine = ozone

## Slide 4: The Clean Air Act
Requires EPA to set National Ambient Air Quality Standards (Standards) for 6 Criteria Pollutants;
These standards are reviewed every 5 years and revised if necessary to protect health and welfare;
Two types of standards
  Primary – protects public health
  Secondary – protects public welfare;
The 6 pollutants are: Carbon Monoxide, Lead, Nitrogen Dioxide, Ozone, Particulate Matter and Sulfur Dioxide
Notes: Maurice suggested that this slide and the next slide be reversed. I have reversed them…see what you think.

## Slide 5: Designation vs. Classification
Designation means that the monitored design value for the area does not meet the current ozone standard
Classification is dependent on the numerical design value and provides the obstacle course and time limit on attaining the standard.
NOTE: Designation historically affects parishes in the MSA where the exceeding monitor resides and emission reduction rules apply in them as well as parishes adjacent to the MSA!

## Slide 6: Classifications and Deadlines
Marginal = 3 years
Moderate = 6 years
Serious = 9 years
Severe = 15 years
Extreme = 20 years
*CAA Sec. 181. Classifications and Attainment Dates

## Slide 7: Classification Requirements - Marginal
Prescriptive Requirements in Clean Air Act
Major Source threshold set at 100tpy of either VOC or NOx
Emissions Inventory submittals required on industrial sources
New Source Review (NSR) permitting requirements
Permit Offsets of 1.1 to 1
Subjects projects to Transportation Conformity
Subjects projects to General Conformity (federal, non-highway projects)

## Slide 8: Classification Requirements - Moderate
Prescriptive Requirements
Must meet Marginal Requirements and:
15% Reduction from Baseline Within 6 Years
RACT on Major Sources
Gasoline RVP of <9.0 psi (State currently conforms except Shreveport)
Stage II Vapor Recovery previously required – May not be needed in future
Vehicle Inspection/Maintenance Program
Permit Offsets of 1.15 to 1

## Slide 9: Costs of Nonattainment on industry
Non-attainment represents a “red flag” in the site selection process for both new facilities and expansions, especially for manufacturing prospects
Non-attainment involves a more complex, expensive environmental permitting process that can reduce the competitiveness of existing business and industry
Once in non-attainment, there is potential risk of significant increases in economic costs (e.g., emissions controls, penalty fees) on industry if air quality does not improve sufficiently over time

## Slide 10: Economic Impact to Transportation and General Construction
Transportation and General Conformity is required make sure that highway and construction projects do not impede the progress that the state is making toward achieving cleaner air quality.
Transportation conformity is required by the Clean Air Act to ensure that federal funding and approval are given to highway and transit projects that are consistent with the air quality goals established by a state air quality implementation plan (SIP).
Emissions budgets are established and projects must conform to those budgets.

## Slide 11: Potential Economic Impact to Consumers
Increased cost to industry translates to increased cost of the products industry produces.
Higher cost of vehicle inspection stickers due to expansion of I/M program.
Increased fuel costs.

## Slide 12: What is the 2008 Ozone Standard
Air quality in area continues to improve
  EPA continues to make standard more stringent
  Announcement December 2013
  Imagine a limbo bar…
8-hour primary ozone standard to 75 parts per billion (ppb) is protective of human health
  1 ppb is equivalent to 1 drop of water in an Olympic sized pool
How is attainment determined?
  Design Value – the 3-year average of the fourth-highest daily maximum 8-hour average ozone concentration measured at each monitor within an area.

## Slide 13: Design Value Chart
Chart: 8-hr Design Value as of December 31, 2010
| LSU | New Roads | French Settlement | Kenner | Dutchtown | Shreveport | Carlyss | Madisonville | Vinton | Carville | B Plaquemine | Garyville | Capitol | Lafayette | Pride | Baker | Dixie | G Tete | Port Allen | Thibodaux | City Park | Hahnville | Chalmette/Arabi | Convent | Monroe | Westlake
 | 78 | 75 | 75 | 75 | 75 | 74 | 74 | 74 | 74 | 73 | 73 | 73 | 73 | 72 | 72 | 72 | 72 | 71 | 71 | 71 | 71 | 70 | 69 | 68 | 64 | 63

## Slide 14: Design Value Chart
Chart: 8-hr Design Value as of December 31, 2011
| LSU | Shreveport | Dutchtown | Capitol | Carville | Kenner | Carlyss | French Settlement | New Roads | Garyville | Dixie | B Plaquemine | Madisonville | Vinton | Pride | Port Allen | Thibodaux | Hahnville | Lafayette | Chalmette/Meraux | City Park | Convent | Westlake | Monroe
 | 82 | 80 | 77 | 77 | 77 | 76 | 76 | 76 | 75 | 75 | 75 | 74 | 74 | 74 | 72 | 72 | 72 | 72 | 72 | 71 | 70 | 69 | 67 | 66





## Slide 15: Current Design Value
Chart: 8-hr Design Value as of December 31, 2012
| LSU | Shreveport | Dutchtown | Carville | New Roads | B Plaquemine | Capitol | Kenner | Garyville | Dixie | Carlyss | French Settlement | Madisonville | Thibodaux | Chalmette/Meraux | Lafayette | Pride | Vinton | Hahnville | City Park | Port Allen | Westlake | Convent | Monroe
 | 79 | 79 | 76 | 76 | 76 | 75 | 75 | 75 | 75 | 75 | 75 | 74 | 74 | 74 | 73 | 72 | 72 | 71 | 71 | 70 | 70 | 69 | 68 | 63





## Slide 16: Design Value Chart
Chart: 8-hr Design Value as of December 31, 2011
| LSU | Shreveport | Dutchtown | Capitol | Carville | Kenner | Carlyss | French Settlement | New Roads | Garyville | Dixie | B Plaquemine | Madisonville | Vinton | Pride | Port Allen | Thibodaux | Hahnville | Lafayette | Chalmette/Meraux | City Park | Convent | Westlake | Monroe
 | 82 | 80 | 77 | 77 | 77 | 76 | 76 | 76 | 75 | 75 | 75 | 74 | 74 | 74 | 72 | 72 | 72 | 72 | 72 | 71 | 70 | 69 | 67 | 66




Chart: Shreveport Area Ozone Design Values, 8-Hour
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
 | 71 | 92 | 88 | 81 | 77 | 79 | 83 | 86 | 86 | 87 | 88 | 85 | 86 | 85 | 86 | 83 | 80 | 82 | 84 | 89 | 92 | 90 | 84 | 80 | 75 | 78 | 80 | 79 | 76 | 72 | 74 | 80

## Slide 17: Ozone Design Values 1980-2011
Chart: Design Value in PPB
| 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
Baton Rouge Area | 125 | 129 | 112 | 105 | 104 | 99 | 96 | 97 | 98 | 98 | 101 | 100 | 99 | 93 | 90 | 91 | 94 | 97 | 96 | 95 | 99 | 91 | 87 | 86 | 89 | 95 | 90 | 89 | 83 | 80 | 78 | 82
Shreveport Area | 71 | 92 | 88 | 81 | 77 | 79 | 83 | 86 | 86 | 87 | 88 | 85 | 86 | 85 | 86 | 83 | 80 | 82 | 84 | 89 | 92 | 90 | 84 | 80 | 75 | 78 | 80 | 79 | 76 | 72 | 74 | 80
Lake Charles Area | 99 | 100 | 99 | 100 | 92 | 92 | 91 | 93 | 94 | 93 | 94 | 94 | 93 | 87 | 86 | 81 | 85 | 85 | 89 | 89 | 84 | 84 | 78 | 80 | 83 | 82 | 80 | 75 | 74 | 74 | 76
New Orleans Area | 91 | 89 | 116 | 104 | 99 | 89 | 89 | 88 | 94 | 91 | 85 | 77 | 80 | 81 | 87 | 84 | 85 | 84 | 85 | 86 | 91 | 89 | 85 | 82 | 82 | 84 | 82 | 83 | 79 | 76 | 75 | 76

## Slide 18: Shreveport MSA Bossier, Caddo and DeSoto
Chart: 2009 Shreveport Area NOx Emissions, tpd
| Area | Nonroad | Onroad | Point | Biogenics
 | 7.3108 | 10.1417 | 18.65 | 28.0027 | 8.0584
Chart: 2009 Shreveport Area VOC Emissions, tpd
| Area | Nonroad | Onroad | Point | Biogenics
 | 21.829 | 11.7643 | 13.38 | 15.9768 | 695.5012

## Slide 19: Recent Activity Regarding O3 Standard
Sierra Club has filed appeal
  EPA denied their request for a reconsideration of the decision not to designate the areas that showed violations from 2009-2011
Appeal filed in US Court of Appeal, DC Circuit
  13-1030 Sierra Club v. EPA, et al

## Slide 20: PM2.5 Standard
Primary and Secondary | Annual | 15 µg/m3 change 12µg/m3 | Annual mean, averaged over 3 years | Attainment
 | 24 – hour | 35 µg/m3 | 98th percentile, averaged over 3 years | 

## Slide 21: PM2.5 Annual Mean Trend
Chart: µg/m3
| 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011
Capitol | 13 | 12.6 | 11.9 | 14 | 12 | 11 | 10 | 11 | 10
Bayou Plaquemine | 11 | 9.9 | 9.9 | 11 | 11 | 10 | 9 | 9 | 9.4
Geismar | 12 | 12.3 | 12.4 | 13 | 12 | 12 | 9 | 11 | 9.9
Hammond | 11 | 10.5 | 11 | 13 | 11 | 10 | 8 | 9 | 9.4
Houma | 11 | 9.8 | 9.5 | 12 | 10 | 9 | 8 | 9 | 8.7
Kenner | 11 | 11.1 | 10.2 | 12 | 10 | 9 | 9 | 9 | 9.2
Lafayette | 11 | 10.2 | 9.7 | 11 | 10 | 9 | 9 | 10 | 9
Lake Charles | 11 | 10.5 | 10 | 11 | 10 | 9 | 9 | 10 | 8.8
Marrero | 12 | 11.3 | 11.1 | 15 | 10 | 9 | 9 | 10 | 9.2
St. Bernard | 10 | 10.9 | 10.2 | 14 | 11 | 11 | 11 | 10 | 10.7
Monroe | 12 | 10.5 | 10.7 | 12 | 11 | 9 | 9 | 10 | 9.4
Port Allen | 13 | 12.9 | 12.2 | 14 | 13 | 11 | 10 | 11 | 11

## Slide 22: Getting back to Attainment
Baton Rouge Area rules
  VOC Controls in DEQ Air Rules – Chapter 21
  NOx Controls in DEQ Air Rules – Chapter 22
DEQ Modeling efforts underway
  Will help determine if these or other rules would be effective in reducing ozone levels in other areas of the state.
Federal Rules help address vehicle emissions and fuel formulations

## Slide 23: Ideas for Emission Reductions
Area Sources
On-road Engines
  Idling Reduction Policies (Schools and Municipalities)
  Alternative Fuels and Repowers (Ethanol, biodiesel and natural gas conversions)
    Bossier City/Parish Natural Gas Conversions
  School Buses, Public Transport and Utilities Truck Retrofits (Diesel Particulate Filters and Oxidation Catalysts)
    Caddo Parish DOCs and Caddo Public Schools Buses DPFs
Non-road Engines
  Requiring use of lower emitting equipment for local projects
  KCS and New Orleans Public Belt Railroad Automatic Engine Start-Stop Switches (Emissions Reductions and diesel fuel savings)
Point Sources
  DEQ existing rules for VOC and NOx
  Voluntary actions by industry
  Consumers using less electricity helps utilities to cut back

## Slide 24: Other Ideas
Ozone Awareness Campaign
  Meteorologist Training
  News Spots highlighting ozone

## Slide 25: Greater Shreveport Clean Air Citizens Advisory Committee (CACAC)
Established by the Mayor of Shreveport in 2000, consisting of representatives from various local stakeholder groups. Goal was to assess air quality issues in Shreveport-Bossier MSA.
Accomplishments
  Developed ozone public awareness campaign including the obtaining of a $15,000 grant for public awareness projects pertaining to ozone issues;
  Obtained a $400,000 federal appropriation for air quality technical support work for the local area, including emission inventory and modeling work;
  Opened communication channels between the Shreveport-Bossier MSA, the EPA and DEQ on air quality planning issues; and
  Obtained formal commitments from the governing bodies of Shreveport, Bossier City, Caddo Parish and Bossier Parish to work cooperatively and, specifically, to develop voluntary measures for the reduction of ozone precursor emissions and enter into an Ozone Flex Agreement with the EPA and LDEQ.

## Slide 26: About the EACs
In 2003 EPA proposed to defer designations for areas not meeting 8-hour standard
  Deferments required areas to reduce ground-level ozone pollution earlier than the Clean Air Act (CAA) required
  Shreveport-Bossier entered into compact
Ruling that the EACs were not legal

## Slide 27: What is the Advance Program?
Ozone Advance is a collaborative effort by EPA, states, tribes and local governments to encourage emission reductions in ozone attainment areas, to help them continue to meet the National Ambient Air Quality Standard (NAAQS).

## Slide 28: What Areas May Get Out Of Participating?
EPA support
Rallying point for public/stakeholder awareness and involvement
Framework for action
Preferred status for DERA grants, see www.epa.gov/cleandiesel/prgnational.htm
Possible recognition
Opportunity to highlight measures/programs already underway along with those undertaken as part of Program
Stakeholder group formation, engagement

## Slide 29: Program Goals
Help attainment areas take action in order to keep ozone and PM levels below the level of the standard to ensure continued health protection
Better position areas to remain in attainment
Efficiently direct available resources toward actions to address ozone problems quickly.

## Slide 30: Why Should Areas Work to Reduce Ozone & PM2.5?
Ensure continued health protection
Less resource intensive to implement measures early
More flexibility to pursue a wide range of options
Proactive
  Could better position some areas to stay in attainment
  If eventually designated, could provide needed reductions that could result in a lower classification and/or that could feed into any eventual SIP
EPA could consider early efforts as a factor in exercising for its discretion to redesignate areas not violating in 2008-10 but violating in later years to nonattainment
Multi-pollutant co-benefits

## Slide 31: Who Can Participate?
States, tribes, local governments
Councils of Government
Other stakeholders, in conjunction with any of the above
“Lead” participant?

## Slide 32: What Are the Criteria for Program Eligibility?
Area must not be nonattainment for either 1997 or 2008 8-hour or PM2.5 standards at the time the they are accepted into the program.
  Maintenance areas
  Eventual Marginal areas
Local entity should generally identify the area
DEQ will identify the monitor(s) that reflect the area’s air quality
Required emissions inventory reporting should be complete (DEQ handles this)

## Slide 33: What Does Participation Mean for You?
Work to Develop a “path forward” plan within a year
Plan should
  Use best efforts to move quickly toward identifying steps that may reduce ozone levels
  Implement path forward, measures/programs as soon as possible
  Collect information as to plan effectiveness
  Informal status check-ins with EPA at least annually

## Slide 34: What Might You Get Out Of Participating?
EPA support
Rallying point for public/stakeholder awareness and involvement
Framework for action
Preferred status for DERA grants, see www.epa.gov/cleandiesel/prgnational.htm
Possible recognition
Opportunity to highlight measures/programs already underway along with those undertaken as part of Program
Stakeholder group formation, engagement

## Slide 35: Model for Today
“As a result of the committee’s recommendations, a formal Intergovernmental Agreement was executed between Shreveport, Bossier City, Caddo Parish and Bossier Parish on June 6, 2002, providing for cooperative planning efforts on air quality matters among all the signatory governing bodies, and, among other things, including a pro rata sharing of the initial costs of a technical consultant to assist with development of the Ozone Flex Plan and a work plan for future technical work.” June 30, 2003 EAC Report to EPA

## Slide 36: Ozone Modeling Project
Conducted primarily for BR Area, but grid includes the entire state
November 14th Presentation
Final product late summer 2013
  Will include scenario for removal of Stage 2 equipment in the 6 parish Baton Rouge area.

## Slide 37: Who is In Advance Program?
Lake Charles – IMCAL and Chamber of Commerce
Shreveport – Chamber of Commerce, Coordinating and Development Corporation, Shreveport, Bossier City
Baton Rouge – CRPC and BRCAC
New Orleans – SCRPD and RPC
Lafayette – still not signed up
Monroe and Alexandria??

## Slide 38: Questions to DEQ about Advance Program
DEQ
Vivian Aucoin: vivian.aucoin@la.gov 225-219-3389
Gilberto Cuadra: gilberto.cuadra@la.gov 225-219-3419
Michael Vince: michael.vince@la.gov 225-219-3482
Mailing Address:
  DEQ Air Permits Division
  Ozone Advance Program
  P. O. Box 4313
  Baton Rouge, LA 70821

## Slide 39: Questions for EPA about Advance Program
EPA Headquarters
  Laura Bunte
  EPA Office of Air Quality Planning and Standards
  (919) 541-0889
  ADVANCE@epa.gov
EPA Region 6
  Carrie Paige
  (214) 665-6521
Website: www.epa.gov/ozoneadvance

## Slide 40: Questions about mobile sources
  Rudy Kapichak
  EPA Office of Transportation and Air Quality
  (734) 214-4574
  kapichak.rudolph@epa.gov