## Slide 1: INTRODUCTION TO RECAP WORKSHOP

## Slide 2: Louisiana Department of Environmental Quality Risk Evaluation/Corrective Action Program October 20, 2003

## Slide 3: RECAP Document
Introduction
  Overview of program
  Use of RECAP
General Guidelines
  Program terminology
  Site ranking system
  Site investigation requirements

## Slide 4: RECAP Document
  Data QA/QC
  Data evaluation and useability
  Identification of the AOI and COC
  Exposure Assessment
  AOIC and CC
  Land use
  Groundwater use
  Groundwater POC and POE

## Slide 5: RECAP Document
  Definitions of SS and RS
  Background concentrations
  Acceptable risk levels
  Identification of toxicity values
  Monitored natural attenuation
  Institutional controls
  Self-implementation
  Demonstration of compliance with RS

## Slide 6: RECAP Document
  Identification of landowners, etc
Screening Option
Management Option 1
Management Option 2
Management Option 3
Ecological Risk Assessment
Soil Re-use

## Slide 7: RECAP Document
Tables
  Table 1 Screening Standards
  Table 2 Soil MO-1 RS
  Table 3 Groundwater MO-1 RS
Figures
Appendix A Site Ranking Example
Appendix B Site Investigation Requirements

## Slide 8: RECAP Document
Appendix C RECAP Forms
Appendix D
  TPH
  PAH
  Lead
  PCDD/PCDF
  Conventional parameters

## Slide 9: RECAP Document
Appendix E NAICS
Appendix F Aquifer Tests
Appendix G Additivity
Appendix H Development/Application of RS
Appendix I MO-2 for UST

## Slide 10: LDEQ’s RECAP
RECAP is a consistent decision-making process for the assessment of, and the response to, environmental contamination that is based on the protection of human health and the environment.

## Slide 11: Use of LDEQ’s RECAP
No Further Action at this time determination
Certification of Completion
Corrective Action Plan approval
Approval of a Closure Plan for a Waste Management Unit

## Slide 12: Overview of LDEQ’s RECAP
Based on national health risk assessment principles/methods
Tiered framework
Lower tiers
  require less information
  protective assumptions
  generic risk-based levels
  often used for screening

## Slide 13: Overview of LDEQ’s RECAP
Higher tiers:
  require more site information
  site-specific EF&T data
     Management Option 2 (MO-2)
  site-specific EF&T and exposure data
     Management Option 3 (MO-3)

## Slide 14: Overview of LDEQ’s RECAP
Screening Option
Management Option 1
Management Option 2
Management Option 3

## Slide 15: Overview of LDEQ’s RECAP
   SO*  MO-2 or MO-3
  
   MO-1  MO-3
  
   MO-2
  
   MO-3

## Slide 16: Overview of LDEQ’s RECAP
Under RECAP, site evaluation
is based on the comparison of:
an “acceptable” constituent concentration
with
the constituent concentration at the site

## Slide 17: Overview of LDEQ’s RECAP
The RECAP document presents the regulations on how the “acceptable” constituent concentration shall be defined and how it will be used to make site management decisions.
“Acceptable” Concentration = Screening Standard
or
RECAP Standard

## Slide 18: Overview of LDEQ’s RECAP
Screening Option  SS
Management Option 1  MO-1 RS
Management Option 2  MO-2 RS
Management Option 3  MO-3 RS
Refer to Section 2.12 for descriptions of SS and RS

## Slide 19: Comparison of SS and RS

## Slide 20: LDEQ’s RECAP
Two fundamental elements of RECAP:
1. Identification of the appropriate RECAP Standard
2. Estimation of the COC concentration at the site

## Slide 21: Step 1
1. Identification of the
RECAP Standard

## Slide 22: Identification of the RECAP Standard
Screening Standards and RECAP Standards are developed for:
protection of human health  RS
prevention of cross-media transfer  RS
protection of resource aesthetics  RS
These standards are compared and the lowest is identified as the Limiting Standard

## Slide 23: Identification of the RECAP Standard
The
Limiting Standard
is the standard that is applied at the site

## Slide 24: Step 2
2. Estimation of the constituent concentration at the site
Step 2 consists of two parts:
2a) Identification of the AOI, then
2b) Estimation of the AOI Concentration (AOIC)

## Slide 25: Step 2a
Step 2a:
Identification of the
Area of Investigation (AOI)

## Slide 26: Step 2b
Step 2b:
Estimation of the
AOI Concentration (AOIC)
or
Compliance Concentration (CC)

## Slide 27: Identification of the AOI Section 2.6.1
SOIL
Step 2a: Identification of the AOI

## Slide 28: Identification of the AOI Section 2.6.1
The AOI is the zone contiguous to, and including, impacted media defined vertically and horizontally by the presence of one or more constituents in concentrations that exceed the limiting standard applicable for the option being implemented.

## Slide 29: AOI Concentration
Soil
  Surface Soil: 0 to 15 ft bgs
  Subsurface Soil: > 15 ft bgs

## Slide 30: Identification of the AOI
Identify limiting standard for option
SO → SS
MO-1 → SS
MO-2 → SS or MO-1 RS
MO-3 → SS, MO-1, or MO-2 RS

## Slide 31: Identification of the AOI
If the areal extent of soil impact > 0.5 acre:
SO → site-specific SS
MO-1 → site-specific SS
MO-2 → site-specific SS
MO-3 → site-specific SS or MO-2 RS

## Slide 32: Identification of the AOI
Compare limiting standard to concentration detected at each sampling location
Identify each location where the concentration > limiting standard
“Connect the dots” to define the horizontal and vertical boundaries of AOI

## Slide 33: Identification of the AOI LRS = 10 ppm
AOI
B2
16 ppm
B4
< 0.005
B3
32 ppm
B7
<0.005
B11
18 ppm
B5
12 ppm
B6
17 ppm
B9
22 ppm
B8
<0.005
B10
<0.005
B17
<0.005
B12
<0.005
B13
29 ppm
B14
18 ppm
B15
15 ppm
B16
1 ppm
B18
2 ppm
B1
55 ppm
B19
<0.005
B20
2 ppm
B21
1 ppm
B22
2 ppm
B23
<0.005
B24
1 ppm
B25
<0.005
B26
<0.005
B27
<0.005
B28
<0.005
B29
<0.005
B30
<0.005

## Slide 34: Identification of the AOI
15’ bgs
B2
14 ppm
B1
33 ppm
B3
12 ppm
B11
11 ppm
B7
<0.01
B4
<0.01
B5
<0.01
B8
2ppm
B13
13 ppm
B16
4 ppm
B18
<0.01
B14
6 ppm

## Slide 35: Identification of the AOI
The RECAP submittal should:
Illustrate all sampling locations and AOI
Summarize AOI data set

## Slide 36: AOI Concentration Sections 2.8.1 and 2.8.2
Soil
Step 2b: Calculation of the AOIC

## Slide 37: AOI Concentration Sections 2.8.1 and 2.8.2
AOIC → Lower of 95% UCL-AM and Max
95% UCL-AM
  what is it?
  why is it used?
  other upper bound estimates of mean

## Slide 38: AOI Concentration Sections 2.8.1 and 2.8.2
AOIC
  Based on all data points on or within the AOI
  Includes ND on or within the AOI
  Does not include data points outside the AOI

## Slide 39: Identification of the AOI LRS = 10 ppm
AOI
B2
16 ppm
B4
< 0.005
B3
32 ppm
B7
<0.005
B11
18 ppm
B5
12 ppm
B6
17 ppm
B9
22 ppm
B8
<0.005
B10
<0.005
B17
<0.005
B12
<0.005
B13
29 ppm
B14
18 ppm
B15
15 ppm
B16
1 ppm
B18
2 ppm
B1
55 ppm
B19
<0.005
B20
2 ppm
B21
1 ppm
B22
2 ppm
B23
<0.005
B24
1 ppm
B25
<0.005
B26
<0.005
B27
<0.005
B28
<0.005
B29
<0.005
B30
<0.005

## Slide 40: AOI Concentration 95% UCL-AM
Dataset for the upper bound estimate of the mean:
B1 55 ppm B7 0.01 ppm
B2 16 ppm B9 22 ppm
B3 32 ppm B11 18 ppm
B4 0.005 ppm B13 29 ppm
B5 12 ppm B14 18 ppm
B6 17 ppm B15 15 ppm

## Slide 41: ProUCL
ProUCL Output for example AOI:
12 samples within the AOI
Data are normally distributed
Statistical recommendation is Student’s t UCL of 27.1 ppm
Max concentration is 55 ppm
AOIC = 27.1 ppm

## Slide 42: Incorrect calculation of AOIC
All data points – within and outside of AOI
Data distribution is non-parametric
95%UCL-AM is 12.5 ppm

## Slide 43: AOI Concentration
RECAP submittal should:
Identify the standards used to delineate the AOI
Illustrate the boundaries of the AOI
Identify data points used to calculate 95%UCL-AM
Present spreadsheet/output of software
Identify the value to be used as the AOIC for comparison to RS

## Slide 44: Groundwater

## Slide 45: Groundwater Classifications
Groundwater Classification 1: public water supply
  Yield > 4,800 g/d
  TDS < 1,000 mg/l
Class 1A: current public water supply
Class 1B: potential public water supply

## Slide 46: Groundwater Classifications
Groundwater Classification 2: domestic water supply
  Yield > 800 g/d but < 4,800 g/d
  TDS < 10,000 mg/l
Class 2A: current domestic water supply
Class 2B: potential domestic water supply (TDS < 1,000)
Class 2C: potential domestic water supply (TDS >1000 but < 10,000)

## Slide 47: Groundwater Classifications
Groundwater Classification 3:
Not a potential public or domestic water supply
Class 3A: yield < 800g/d
Class 3B: TDS > 10,000 mg/l

## Slide 48: Groundwater/Aquifer Use Section 2.10
Current Use:
  DOTD Well Survey (1 mi radius/12 mo)
  500 foot walking receptor survey
Potential Use:
  sustainable yield
  total dissolved solids

## Slide 49: Compliance Concentration Section 2.8.3
Groundwater
Step 2a: Identification of the AOI
(same as for soil)
*Note: the AOIC for groundwater is referred to as the
Compliance Concentration (CC)

## Slide 50: Compliance Concentration Section 2.8.3
Groundwater
Step 2b:Estimation of AOI Concentration
(NOT the same as for soil)

## Slide 51: Compliance Concentration Section 2.8.3
Step 2b:
Compliance Concentration is the concentration detected at the point of compliance
POC should located at or near the source (Max concentration)
CC is the concentration that is compared to the RS
CC is a single point max concentration NOT a 95%UCL-AM concentration

## Slide 52: Groundwater: POC and POE Section 2.11
Point of Compliance
  point where RECAP standard must be met; CC at the POC must equal the RS to comply with RECAP
Point of Exposure
  point of actual or potential contact between a receptor and a COC

## Slide 53: Groundwater 1: POC and POE
Point of Exposure:
  throughout the aquifer to be protected or restored
Point of Compliance:
  sampling location placed as near to the source as feasible without causing an adverse impact

## Slide 54: Groundwater2: POC and POE
Point of Exposure:
  on-site exposure point, or
  property boundary, or
  nearest downgradient point off-site
Point of Compliance:
  sampling location placed as near to the source as feasible without causing an adverse impact

## Slide 55: Groundwater 3: POC and POE
Point of Exposure:
  point of discharge to a surface water body within the aquifer
  a point in the aquifer
  use of a mixing zone to demonstrate compliance is not allowed under RECAP
Point of Compliance:
  sampling location placed as near to the source as feasible without causing an adverse impact

## Slide 56: Point of Compliance and Point of Exposure Section 2.11
GW-1
GW-2
GW-3
Road
Water Body
POC
POC
POC
POC
POE
POE
POE
Flow Direction
Flow Direction
Flow Direction
POE THROUGHOUT AQUIFER
Site Boundaries

## Slide 57: Dilution Factors
Numerical estimation of the reduction in chemical concentration associated with groundwater migration
DF2:
  Applicable to GW 2 zones
  Accounts for reduction in chemical concentration as groundwater migrates from the source area to the nearest downgradient property boundary
  GW2, SoilGW2

## Slide 58: Dilution Factors GW 2 Zone
Property boundary
(POE)
(Must meet
DW standard at this point)
0.005 mg/l
Source
(POC)
(Can leave
0.005 x 111 = 0.56 mg/l at POC and meet DW standard at POE)
Dilution factor (DF2)
111 x ↓
900 ft

## Slide 59: Section 2.17
Institutional Controls for Groundwater
GW2 Zone - if COC concentrations within the property boundaries > GW2 RS, then conveyance notice required.

## Slide 60: Dilution Factors
DF3:
  Applicable to GW 3 zones
  Accounts for reduction in chemical concentration as groundwater migrates from the source area to the nearest downgradient surface water body
  GW3DW, GW3NDW, SoilGW3DW, SoilGW3NDW

## Slide 61: Dilution Factors GW 3 Zone
Surface Water
(POE)
(Must meet
RS standard at this point)
0.1 mg/l
Source
(POC)
(Can leave
0.1 x 440 = 44 mg/l at POC and meet RS standard at POE)
Dilution factor (DF3)
440 x ↓
1800 ft

## Slide 62: MO-1Default DF
Appendix H
Based on:
  Thickness of the groundwater plume (Sd)
  Distance from POC to POE

## Slide 63: Estimation of Sd
Sd = Thickness of impacted groundwater within permeable zone
Un-impacted groundwater
10’
15’
Impacted groundwater
5’
Sd = 5’

## Slide 64: Estimation of Sd
Sd = Thickness of permeable zone if thickness is not known or if the zone is not impacted
Un-impacted groundwater
10’
15’
Sd = 15’

## Slide 65: MO-1 DF Appendix H

## Slide 66: Dilution Factors
May be applied to:
  GW2
  GW3DW
  GW3NDW
  SoilGW2
  SoilGW3DW
  SoilGW3NDW

## Slide 67: Dilution Factors
May NOT be applied to other groundwater or soil RS or SS:
  GWair
  GWes
  Watersol
  Soilni
  Soili
  Soiles
  Soilsat

## Slide 68: Chemicals of Concern (COC)

## Slide 69: Identification of COC Section 2.6.2
COC = Constituents of Concern
COC are constituents included in RECAP assessment
Id of COC based on options completed and/or the option being implemented

## Slide 70: Identification of the COC
A COC is a chemical present at a concentration that exceeds the SS or RS being applied at the AOI.
A chemical demonstrated to be present at a concentration that is less than the SS or RS being applied at the AOI is eliminated from further consideration.

## Slide 71: Identification of the COC
The list of COC may be modified:
Reduced COC list for modeling purposes (MO-3)
Based on site-specific background concentrations
SQLs

## Slide 72: Land Use

## Slide 73: Land Use
Why is land use important?
Determines exposure
Exposure determines acceptable soil concentration (SS or RS)
Industrial exposure: 250 d/yr, 25 yr
Non-industrial exposure: 350 d/yr, 30yr, child
↑ Exposure → ↓ soil standard

## Slide 74: Land Use Section 2.9
Land use must be determined to apply SS or RS
Industrial/Commerical land use
Non-industrial/residential land use
North American Industry Classification System (NAICS)
Appendix E

## Slide 75: Land Use Section 2.9
Current and future use must be considered
If land is undeveloped:
  Zoning/development plans
  Surrounding land use
  Assume non-industrial

## Slide 76: Land Use Section 2.9
If land use changes - LDEQ notified and AOI re-evaluated
Section 2.17 - if COC concentrations > non-industrial standard then conveyance notice required

## Slide 77: Consideration of Background Levels Under RECAP

## Slide 78: Background Concentrations Section 2.13
Background samples:
Collected in the vicinity of the AOI
Not collected in impacted areas
Share the same basic characteristics as the medium of concern
Must be approved by the Department
Literature values unacceptable

## Slide 79: Background Concentrations Section 2.13
How should background data be used?
  Calculate arithmetic average concentration for background data for < 7 data points
  Calculate the arithmetic average + 1SD for > 8 data points

## Slide 80: Background Concentrations Section 2.13
How should background data be used?
  Compare to arithmetic average concentration for AOI
  If limiting SS or RS < background, then background is used as the SS or RS
  Background concentrations applied at an AOI are subject to Dept approval
  Arsenic

## Slide 81: RECAP Screening Option and Management Options

## Slide 82: RECAP Screening Option Section 3.0 Appendix H

## Slide 83: Screening Option: Criteria for Management
Soil and GW (air) only
  Air emissions from soil are indirectly addressed
2. No COC discharge to SW via GW
3. Area of soil investigation < 0.5 acre
  Q/C
  Exceptions: inorganics, LSS based on QL, saturation level, ceiling value, or background

## Slide 84: Screening Option: Criteria for Management
4. Declining conditions
  Source removed
  COC mass is not increasing
  Area of COC concentration > SS is not expanding
5. Non-industrial or industrial scenario
  No other scenarios may be evaluated using SS
6. No exposure to soil and gw
  SS do not account for exposure via 2 media

## Slide 85: Screening Option: Criteria for Management
7. No other pathways
  Only soil contact and household groundwater use
8. No unusual site conditions
  Exposure at AOC similar to SO assumptions
  EF&T conditions at AOC similar to SO assumptions

## Slide 86: Screening Standards
Soil and groundwater SS
Industrial and non-industrial
Table 1

## Slide 87: SO: Appendix H
If a chemical is not listed in Table 1, SS should be calculated using the equations and assumptions in App H
No substitutions may be made for the input parameters in App H
  Exception: site-specific area of impacted soil

## Slide 88: SO: Appendix H
Toxicity values – Integrated Risk Information System (IRIS)
http://www.epa.gov/iris/subst/index.html

## Slide 89: Screening Option SOIL

## Slide 90: Soil Screening Standards Table 1
SoilSSni or SoilSSi
risk-based values (inhalation, dermal, ingestion)
SoilSSni = soil screening standard for non-industrial land use
SoilSSi = soil screening standard for industrial land use
Have been adjusted downward to account for additivity

## Slide 91: Soil Screening Standards Table 1
SoilSSGW
  protective of GW 1 zone
  applicable to all groundwater zones regardless of classification
(Soilsat)
  protection of aesthetics
  not separate SS
Background levels, QLs

## Slide 92
Screening Option
Soil
Screening Process

## Slide 93: Identification of the Soil Limiting Screening Standard
Identification of the Limiting Soil SS
How to use Table 1:
Identify the SoilSSni or SSi and SoilSSGW
Id the lower of the SoilSSni or SSi and SoilSSGW
This value is the soil limiting SS (LSS)

## Slide 94: SO: Identification of the Soil AOI Concentration
Identification of AOI Concentration:
  Maximum concentration detected in soil

## Slide 95: Screening Process: Soil
Compare maximum concentration detected in soil to LSS:
  If max < LSS for all chemicals, then NFA
  If max > LSS, then the COC is evaluated under MO-1, 2, or 3 (or remediated to LSS)
  If the max concentration for a chemical < LSS, then that chemical is “screened out”

## Slide 96: SO: Soil Screening Example
  XYZ Facility: release of acetone to soil
  Soil data:
  SB-1 80 ppm
  SB-2 65 ppm
  SB-3 21 ppm
  SB-4 17 ppm
  SB-5 1 ppm
  SB-6 0.5 ppm

## Slide 97: Identification of the AOIC
For the SO, the AOIC is the max concentration
  Soil data:
  SB-1 80 ppm
  SB-2 65 ppm
  SB-3 21 ppm
  SB-4 17 ppm
  SB-5 1 ppm
  SB-6 0.5 ppm

## Slide 98: Identification of the Soil LSS
Industrial land use; COC is acetone
Table 1:
Id the SoilSSi = 1400 mg/kg
Id the SoilSSGW = 1.5 mg/kg
Id the lower of SoilSSi and SoilSSGW = 1.5 mg/kg
This value is the soil limiting SS (LSS)

## Slide 99: Soil Screening Process
Compare maximum concentration detected in soil to LSS:
  AOIC = 80 ppm
  LSS = 1.5 mg/kg
  80 mg/kg >1.5 mg/kg
  Acetone needs to be evaluated under MO-1, 2, or 3 (or remediated to LSS)

## Slide 100: Screening Option GROUNDWATER

## Slide 101: Groundwater Screening Standard Table 1
GWSS
  risk-based (MCL or ingestion, inhalation)
  protective of GW 1 zone
  applicable to all zones regardless of classification
(Watersol)
  water solubility
  based on aesthetics – prevention of NAPL
  not a separate SS

## Slide 102: Groundwater Screening Standard Other considerations
Background levels
Quantitation Limits

## Slide 103: Screening Option Groundwater Screening Process

## Slide 104: Identification of the GW Limiting Screening Standard
Identification of the Limiting Groundwater SS
How to use Table 1:
1. Identify the GWSS
  This value is the limiting groundwater SS

## Slide 105: SO: Identification of the Compliance Concentration
Id of Compliance Concentration (CC):
  Concentration detected at the POC
  = maximum concentration at the AOI
  NOT the 95%UCL-AM concentration

## Slide 106: GW Screening Process
Compare compliance concentration to LSS:
  If CC < LSS for all chemicals, then NFA
  If CC > LSS, then the COC is evaluated under MO-1, 2, or 3 (or remediated to LSS)
  If the max concentration for a chemical < LSS, then that chemical is “screened out”

## Slide 107: SO GW Screening Example
XYZ Facility: release of acetone to soil that has impacted shallow GW
GW data:
SB-1 55 mg/l
SB-2 45 mg/l
SB-3 30 mg/l
SB-4 10 mg/l
SB-5 3 mg/l
SB-6 0.75 mg/l

## Slide 108: Identification of the GW Compliance Concentration
Identification of POC
Identification of the CC (COC concentration at POC)
GW data:
SB-1 55 mg/l
SB-2 45 mg/l
SB-3 30 mg/l
SB-4 10 mg/l
SB-5 3 mg/l
SB-6 0.75 mg/l

## Slide 109: Identification of the GW Limiting Screening Standard
COC = acetone
Table 1:
1. Identify the GWSS = 0.1 mg/l
  This value is the limiting groundwater SS

## Slide 110: SO GW Screening
Compare compliance concentration to LSS:
  CC = 55 mg/l
  LSS = 0.1 mg/l
  55 mg/l > 0.1 mg/l, therefore acetone needs to be evaluated under MO-1, 2, or 3 (or remediated to LSS)

## Slide 111
Management Option 1
Section 4.0
Appendix H
RECAP

## Slide 112: Management Option 1 Criteria for Management
Soil and GW only
  Air emissions from soil and gw addressed
2. No COC discharge to SW via GW
  RECAP standards do not allow COC discharge to SW
3. Area of soil investigation < 0.5 acre
  Q/C and DF2 and DF3
  Exceptions: inorganics; LRS based on QL, saturation level, ceiling value, bg level, Soilgw1

## Slide 113: Management Option 1 Criteria for Management
4. Declining conditions
  Source removed/COC mass is not increasing
5. Non-industrial or industrial
  No other exposure scenarios may be evaluated under MO-1
6. No other exposure pathways
  MO-1 RS only address direct contact with soil and household use of groundwater
  Does not address particulate emissions, surface water, sediment, etc.
7. No unusual site conditions
Refer to Section 4.1 for more info

## Slide 114: Management Option 1 RECAP Standards
Soil and Groundwater RS
Industrial and non-industrial land use
Soil RS - Table 2
Groundwater RS - Table 3
If a COC is not in Tables 2 and 3 - Appendix H

## Slide 115: MO-1 Soil Assessment

## Slide 116: MO-1: Id of the Soil COC
COC for the MO-1 soil assessment:
All chemicals whose max concentration in soil > limiting soil SS

## Slide 117: Management Option 1
Identification and Application of the
Limiting Soil RECAP Standard
Table 2
Appendix H

## Slide 118: MO-1 Soil RECAP Standards Section 4.2.1
Soilni or Soili
  Soilni = soil standard for non-industrial land use
  Soili = soil standard for industrial land use
  risk-based (inhalation, ingestion, dermal contact)
  must consider additive effects for noncarcinogens, foonoted with “N”

## Slide 119: MO-1 Soil RECAP Standards Section 4.2.1
SoilGW1= soil standard protective of groundwater 1 zone
SoilGW2 x DF2 = soil standard protective of groundwater 2 zone
SoilGW3DW x DF3 = soil standard protective of groundwater 3 zone that potentially discharges to a surface water body classified for as a drinking water source
SoilGW3NDW x DF3 = soil standard protective of groundwater 3 zone that potentially discharges to a surface water body classified for as a non-drinking water source

## Slide 120: MO-1 Dilution factors
DF2 = dilution factor to account for dilution of COC concentration in a groundwater 2 zone due to migration from the source to nearest downgradient property boundary
DF3 = dilution factor to account for dilution of COC concentration in a groundwater 3 zone due to migration from the source to nearest downgradient surface water body

## Slide 121: MO-1 Soil RECAP Standards Section 4.2.1
Soilsat
  Soilsat = soil saturation
  Based on protection of resource aesthetics – prevention of NAPL
Soiles
  Standard for volatile emissions from soil to an enclosed structure
  Enclosed structure - an occupied (or potentially occupied) [i.e., one or more receptors spend a significant portion of the day (or workday) within the enclosed structure] structure on a slab foundation that has a roof and walls on all sides which prevent the free exchange of indoor air with outdoor (ambient) air.
  In general, applicable to soil < 15 ft bgs
  In general, volatile = HLC > 1E-05 atm-m3/mole and mw < 200 g/mole

## Slide 122: MO-1 Soil RECAP Standards Section 4.2.1
Background levels
  If MO-1 LRS for inorganic COC < BG
  Comply with Section 2.13
Quantitation limits
  If MO-1 RS < QL, then default to QL
  QL subject to Dept approval
Ceiling values
  TPH - 10,000 ppm

## Slide 123: Id of the limiting MO-1 Soil RECAP Standard Table 2
  Soili (Footnote N)
  Soilni (Footnote N)
  SoilGW1
  SoilGW2 (Footnote x DF2)
  SoilGW3 (Footnote x DF3)
  Soilsat
+/- Soiles
Limiting RS = lower of these 3 RS
Additivity
See Appendix G
See Appendix H
for DF2 and DF3
Applicable to liquids

## Slide 124: Management Option 1
Identification of the Soil AOIC
Section 2.8.2

## Slide 125: Management Option 1
MO-1 Soil AOIC:
  95% UCL-AM concentration
  If 95%UCL-AM > Maximum concentration, then maximum concentration shall be used as the AOIC

## Slide 126: Management Option 1 Soil Screening
MO-1 Screening: Compare the soil AOIC to the limiting soil RS:
  If AOIC < limiting RS for all COC, then NFA
  If AOIC > limiting RS, then proceed to MO-2 or 3 or remediate to MO-1 LRS

## Slide 127: Soil to Groundwater Pathway SPLP Data
SPLP data should be representative of max concentration
How is the SPLP data used to evaluate the soil to gw pathway?
  SoilGW1: Compare SPLP to GW1 x DFSummers
  SoilGW2: Compare SPLP to GW2 x DFSummers x DF2
  SoilGW3: Compare SPLP to GW3 x DFSummers x DF3

## Slide 128: Soil to Groundwater Pathway SPLP Data
  If SPLP <, then screen out soil to gw pathway
  If SPLP >, then delineate area of concern
  SPLP vs TCLP
  SPLP vs LRS
  Appendix H

## Slide 129: MO-1 Soil Screening Example
  ABC Facility had a release of toluene to soil
  First zone is classified as a GW3 aquifer
  Thickness of the groundwater plume is 5 ft (Sd = 5 ft)
  Distance from source to SW is1200 ft
  Surface water body has a drinking water designation

## Slide 130: MO-1 Soil Screening Example
Soil data (mg/kg):
SB-1 210
SB-2 350
SB-3 530
SB-4 300
SB-5 275
SB-6 112
SB-7 103
SB-8 62
SB-9 5
SB-10 2

## Slide 131: MO-1 Soil Screening Example
Identification of the AOIC:
95%UCL-AM concentration = 294 mg/kg
Max concentration = 530 mg/kg
AOIC = 294 mg/kg

## Slide 132: MO-1 Soil Screening Example
Identification of the Limiting RECAP Standard:
Table 2: Soili = 4800 mg/kg
SoilGW3DW = 120 x DF3 of 173 = 20,760 mg/kg
Soilsat = 520 mg/kg
Limiting RS (LRS) = 520 mg/kg (lower of the 3 RS)

## Slide 133: MO-1 Soil Screening Example Identify DF3: Sd = 5Ft; distance = 1200 ft

## Slide 134: MO-1 Soil Screening Example
Compare the AOIC to the LSS:
AOIC = 294 mg/kg
LSS = 520 mg/kg
294 mg/kg < 520 mg/kg
NFA-ATT for toluene in soil

## Slide 135: MO-1 Soil Screening Example using SPLP data
  XXX Facility had a release of chlorodibromomethane to soil
  First zone is classified as a GW3 aquifer
  Thickness of the first groundwater zone is 4 ft (Sd = 4 ft)
  Distance from source to SW is 1760 ft
  Surface water body has a non-drinking water designation
  DF3 = 440
  SPLP test results: 16 mg/l

## Slide 136: MO-1 Soil Screening Example using SPLP data
  SoilGW3: Compare SPLP to GW3 x DFSummers x DF3:
  SPLP test results = 16 mg/l
  GW3NDW = 5E-03 mg/l (Table 3)
  5E-03mg/l x 20 x 440 = 44 mg/l
  44 mg/l acceptable SPLP value
  16 mg/l < 44 mg/l
  Soil to groundwater pathway is screened out for this COC

## Slide 137: Management Option 1
MO-1
Groundwater Assessment

## Slide 138: MO-1: Id of the GW COC
COC for the MO-1 groundwater assessment:
All chemicals whose max concentration in groundwater > GWSS

## Slide 139: Management Option 1
Identification and Application of the
Limiting GW RECAP Standard
Table 3
Appendix H

## Slide 140: MO-1 Groundwater RS Section 4.2.2 and Table 3
GW1
  GW 1 zone
  risk-based or MCL
  Footnote “N” (noncarcinogen) - additivity
GW2
  GW 2 zone
  risk-based or MCL
  DF2 (source to property boundary)
  Footnote “N” - additivity

## Slide 141: MO-1 Groundwater RS Section 4.2.2 and Table 3
GW3DW and GW3NDW
  GW 3 zone
  discharge to SW
  DF3 (source to SW)
  LAC 33:IX, §1123, Table 3 for SW designated use
Watersol
  GW 1, 2, and 3
  Aesthetics – prevention of free product

## Slide 142: MO-1 Groundwater RS
GWair = standard for emissions from shallow gw to ambient air
GWes= standard for volatile emissions from groundwater to an enclosed structure
  Enclosed structure - an occupied (or potentially occupied) [i.e., one or more receptors spend a significant portion of the day (or workday) within the enclosed structure] structure on a slab foundation that has a roof and walls on all sides which prevent the free exchange of indoor air with outdoor (ambient) air.
  In general, applicable to soil < 15 ft bgs
  In general, volatile = HLC > 1E-05 atm-m3/mole and mw < 200 g/mole

## Slide 143: MO-1 Groundwater RS Other considerations
Background levels
Quantitation limits
If GW3 x DF3 < GW2, then use GW2

## Slide 144: MO-1 Groundwater Screening

## Slide 145: MO-1 Limiting GW RECAP Standard Table 3
  GW1 (Footnote N)
  GW2 (Footnote x DF2)
  GW3 (Footnote x DF3)
  GWair (Footnote N)
  S (Watersol)
Limiting groundwater RS = lower of the 3 RS
See Appendix H
for DF2 and DF3
Additivity: See Appendix G

## Slide 146: Identification of the MO-1 Limiting Groundwater RS
GW1 Zone
  lower of GW1 and Watersol
GW2 Zone
  lower of GW2 x DF2 and Watersol (+/- GWair or GWes)
GW3 Zone
  lower of GW3 x DF3, GWair, and Watersol (+/- GWes)

## Slide 147: MO-1: Id of the GW Compliance Concentration
Compliance Concentration:
  Concentration detected at the POC
  Maximum concentration
  NOT 95%UCL-AM concentration

## Slide 148: Management Option 1 GW Screening
Compare the compliance concentration to the limiting RS:
  If CC < LRS for all COC, then NFA
  If CC > LRS, then proceed to MO-2 or 3 or remediate to MO-1 LRS

## Slide 149: Management Option 1 GW Screening GW 1 Example
JXJ Facility had a release of benzene to a GW 1 zone located 50 ft bgs; Sd = 5 ft; distance to property boundary is 1400 ft; distance to SW is 3200 ft; SW is classified as non-DW source.
Groundwater data:
SB-1 (POC) 0.06 mg/l (CC)
SB-2 0.002 mg/l
SB-3 0.05 mg/l
SB-4 0.04 mg/l
SB-5 0.01 mg/l

## Slide 150: Management Option 1 GW Screening GW 1 Example
Identification of the LRS for GW1 zone:
GW1 = 5E-03 mg/l
Watersol = 1800 mg/l
LRS = 5E-03 mg/l
Screening - Compare CC to LRS:
0.06 mg/l > 5E-03 mg/l so need to remediate.
Note: POE – throughout aquifer

## Slide 151: Management Option 1 GW Screening GW 2 Example
JXJ Facility had a release of benzene to a GW 2 zone located 30 ft bgs; Sd = 10 ft; distance to property boundary is 1400 ft; distance to SW is 3200 ft; SW is classified as non-DW source.
Groundwater data:
SB-1 (POC) 0.6 mg/l (CC)
SB-2 0.3 mg/l
SB-3 0.28 mg/l
SB-4 0.4 mg/l
SB-5 0.12 mg/l

## Slide 152: Management Option 1 GW Screening GW 2 Example
Identification of the LRS for GW2 zone:
GW2 = 5E-03 mg/l x DF2 of 124 = 0.62 mg/l
Watersol = 1800 mg/l
LRS = 0.62 mg/l
Screening - Compare CC to LRS:
0.6 mg/l < 0.62 mg/l so NFA-ATT
Note: POE – nearest downgradient property boundary

## Slide 153: Management Option 1 GW Screening GW 2 Example

## Slide 154: Management Option 1 GW Screening GW 3 Example
JXJ Facility had a release of benzene to a GW 3 zone located 10 ft bgs; Sd = 5 ft; distance to property boundary is 1400 ft; distance to SW is 3200 ft; SW is classified as non-DW source.
Groundwater data:
SB-1 (POC) 61 mg/l (CC)
SB-2 29 mg/l
SB-3 53 mg/l
SB-4 41 mg/l
SB-5 37 mg/l

## Slide 155: Management Option 1 GW Screening GW 3 Example
Identification of the LRS for GW3 zone:
GW3NDW = 1.3E-02 mg/l x DF3 of 440 = 5.7 mg/l
Watersol = 1800 mg/l
GWair = 390 mg/l
LRS = 5.7 mg/l
Screening - Compare CC to LRS:
61 mg/l > 5.7 mg/l so need to evaluate under MO-2 or MO-3
Note: POE – nearest downgradient surface water body

## Slide 156: Management Option 1 GW Screening GW 3 Example

## Slide 157
Management Option 2
Section 5.0
Appendix H
RECAP

## Slide 158: Management Option 2: Criteria for Management
1. Soil and GW (air) only
2. No COC discharge to SW via GW
3. Area of soil investigation < 0.5 acre
4. Declining conditions
5. Non-industrial or industrial
6. No other exposure pathways
7. No unusual current or future site conditions

## Slide 159: Management Option 2 RECAP Standards
  Soil and groundwater RS
  Industrial and non-industrial land use
  Site-specific EF&T data
  Appendix H
  NO lookup tables in RECAP

## Slide 160: MO-2: Appendix H
No substitutions may be made for the exposure parameters
  Soilni and Soili
  Soiles
  GW1, GW2, GW3DW, GW3NDW
  GWes
Exception: site size (VF, PEF)
Tox values - IRIS

## Slide 161: MO-2: Appendix H
Site-specific data may be used for EF&T parameters
  SoilGW
  Soiles
  Soilsat
  GWes
  DAF
In the absence of site-specific data, default values presented in App H shall be used

## Slide 162: Site-specific EF&T data MO-2
Examples of site-specific data that may be used under MO-2:
Source size
foc – fraction of organic carbon
Soil particle density
Water-filled soil porosity
Dry soil bulk density

## Slide 163: Management Option 2 Soil Assessment

## Slide 164: MO-2: Id of the Soil COC
COC for the MO-2 soil assessment:
All chemicals whose max concentration in soil > limiting soil MO-1 LRS

## Slide 165: MO-2 Soil RECAP Standards
Soilni or Soili
  risk-based (additivity)
Soilni-PEF or Soili-PEF
  standard for inhalation of soil particulates
  risk-based (additivity)
SoilGW1, SoilGW2, or SoilGW3DW/SoilGW3NDW
  based on GW zone to be protected
  site-specific: 4 methods – App H
  site-specific DAF2, DAF3

## Slide 166: MO-2 Soil RECAP Standards
Soilsat
  resource aesthetics
  site-specific
  soil (0 to depth of impact)
Soiles
  risk-based (additivity)
  soil beneath an enclosed structure
  volatiles in surface soil
Background levels; quantitation limits

## Slide 167: Id of the MO-2 soil Limiting RECAP Standard
  Soili (Footnote N)
  Soilni (Footnote N)
  SoilGW1
  SoilGW2 (Footnote x DF2)
  SoilGW3 (Footnote x DF3)
  Soilsat
+/- Soiles
Limiting RS = lower of these 3 RS
Additivity
See Appendix G
See Appendix H
for DF2 and DF3
Applicable to liquids

## Slide 168: Management Option 2 Section 2.8.2
MO-2 Soil AOIC:
  95% UCL-AM concentration
  If 95%UCL-AM > Maximum concentration, then maximum concentration shall be used as the AOIC

## Slide 169: Management Option 2 Soil Screening
MO-2 Screening: Compare the soil AOIC to the limiting soil RS:
  If AOIC < limiting RS for all COC, then NFA
  If AOIC > limiting RS, then proceed to MO-3 or remediate to MO-2 LRS

## Slide 170: MO-2 Groundwater Assessment

## Slide 171: Management Option 2 Groundwater RECAP Standards
GW1
  GW 1 zone
  risk-based or MCL
  additivity
GW2
  GW 2 zone
  risk-based or MCL
  site-specific DAF2 (source to property boundary)
  additivity

## Slide 172: Management Option 2 Groundwater RECAP Standards
GW3DW GW3NDW
  GW 3 zone
  Prevent discharge to SW
  site-specific DAF3 (source to SW)
Watersol
  Appliable to GW 1, 2, and 3 zones
  Aesthetics – prevention of free product

## Slide 173: Management Option 2 Groundwater RECAP Standards
GWes
  risk-based (additivity) – focus is indoor air COC
  groundwater beneath enclosed space
  volatiles; < 15 ft bgs
GWair
  risk-based (additivity)
  volatiles; < 15 ft bgs
Background levels
Quantitation limits

## Slide 174: MO-2 Identification of the Limiting Groundwater RS
GW1 Zone
  lower of GW1 and Watersol (+/- GWair or GWes)
GW2 Zone
  lower of GW2 and Watersol (+/- GWair or GWes)
GW3 Zone
  lower of GW3, GWair, and Watersol (+/- GWes)

## Slide 175: MO-2 Id of the Compliance Concentration
Compliance Concentration:
  Maximum concentration detected = concentration at POC
  NOT the 95%UCL-AM concentration

## Slide 176: Management Option 2 Groundwater Screening
Compare the CC to the LRS:
If CC for all chemicals < LRS, then NFA
If CC > LRS, then proceed to MO-3 or remediate to MO-2 LRS

## Slide 177: RECAP
Management Option 3
Section 6.0
Appendix H

## Slide 178: Management Option 3: Criteria for Management
1. Soil and groundwater (air) only
2. No groundwater discharge to surface water
3. Area of soil investigation < 0.5 acre
4. Declining conditions
5. Non-industrial or industrial scenario
6. Same receptor is not exposed to soil and gw
7. No other exposure pathways
8. No unusual current or future site conditions

## Slide 179: Management Option 3
Site-Specific MO-3 RECAP Standards
Site-specific EF&T data
Site-specific exposure data
May involved sophisticated modeling
Often complex assessments
Review - Toxicological Services Group

## Slide 180: Workplans
Not required for SO, MO-1, and simple MO-2
Recommended for complex MO-2
Required for all MO-3
The more specifics the better: COC, conceptual site model, toxicity data, all exposure and EF&T assumptions, methods, models, etc.
Approval of Workplan required

## Slide 181: A Site-Specific MO-2 RECAP Evaluation for Typical UST Sites Appendix I
RECAP
Notes: I’d like to give you a brief overview of the RECAP Program and then Dr. Sutherlin will present a more detailed review.

## Slide 182: Appendix I
MO-2 assessment for typical UST sites
Separate RS tables
  Soili, Soilni, SoilGW, Soilsat
  GW1, GW2, GW3, Watersol
  Soiles, Soil-PEF, and GWes – no App I RS but can be evaluated under MO-2

## Slide 183: Appendix I
Site-specific data
  source length
  source width
  foc
16 Category Tables for RS

## Slide 184: Additivity
1 + 1 + 1 = 3

## Slide 185: What is additivity? Why is it important?

## Slide 186: MO-1 and MO-2 RS
Represent an acceptable exposure level for exposure to a single chemical via a single medium
Do not address additivity due to exposure to multiple chemicals or multiple exposure media
RS do address exposure via multiple pathways

## Slide 187: MO-1 and MO-2 RS
Risk-based RS based on noncarcinogenic health effects must be adjusted to account for additivity effects
  Soilni, Soili, Soiles
  GW1, GW2, GWair, GWes
  Footnoted in Tables 2 and 3 by “N”
Not applicable to SoilGW, Soilsat, GW3, Watersol, background levels, quantitation limits, MCLs, ceiling values

## Slide 188: MO-1 and MO-2 RS
Refer to Section 2.14 and Appendix G for additional info
Incorrect adjustment of RS to account for additivity is one of the most common reasons for NODs

## Slide 189: MO-1: Accounting for Additivity
Modification of risk-based MO-1 RS:
  group noncarcinogenic chemicals by target organ/critical effect

## Slide 190: MO-1: Accounting for Additivity
1. Identify the target organ/critical effect for each noncarcinogenic chemical (RfD)
  http://www.epa.gov/iris/subst/index.html
  Example from IRIS - Toluene
I.A.1. Oral RfD Summary
Critical Effect Experimental Doses *UF RfD
Increased kidney weight BMDL: 238 mg/kg-day 3000 0.08 mg/kg-day BMD: 431 mg/kg-day
13-week gavage study in rats (NTP, 1990)

## Slide 191: MO-1: Accounting for Additivity
2. Group the chemicals by target organ/critical effect
3. Divide the RS by the number of chemicals affecting the same target organ

## Slide 192: MO-1: Accounting for Additivity Example
Step 1 Identify the target organs
Chemical Target Organ
A kidney
B kidney, liver
C CNS
D kidney

## Slide 193: MO-1: Accounting for Additivity Example
Step 2 Group chemicals by target organ
Kidney: A, B, D
Liver: B
CNS: C
3 chemicals affect the kidney (additive effects)
1 chemical affects the liver (no additivity)
1 chemical affects the CNS (no additivity)

## Slide 194: MO-1: Accounting for Additivity Example
Chemical Target Organ RS Adjusted RS
A kidney 24 24/3 = 8
B kidney, liver 15 15/3 = 5
C CNS 10
D kidney 60 60/3 = 20
Divide the RS for A, B, and D by 3 (kidney)

## Slide 195: MO-1 Additivity Example
Acetone, cadmium, chlorobenzene and 1,1-DCE are present in residential soil; all have Soilni based on noncarinogenic effects
Step 1- Identify health effect targets (App G Table G-1):
Acetone: liver, kidney
Cadmium: kidney
Chlorobenzene: liver
1,1-DCE: liver

## Slide 196: MO-1 Additivity Example
Step 2 – Summarize by targets:
(3) Liver: acetone, chlorobenzene, 1,1-DCE
(2) Kidney: acetone, cadmium
Acetone Soilni needs to be divided by 3 (liver)
Chlorobenzene Soilni needs to be divided by 3 (liver)
1-1, DCE Soilni needs to be divided by 3 (liver)
Cadmium Soilni needs to be divided by 2 (kidney)

## Slide 197: MO-1 Additivity Example
Step 3 – Adjust Soilni to account for additivity:
Table 2 Soilni Adjusted Soilni
Acetone 1700 1700/3 = 567
Cadmium 39 39/2 = 19.5
Chlorobenzene 170 170/3 = 57
1,1,-DCE 130 130/2 = 65

## Slide 198: RECAP Submittal Requirements

## Slide 199: Submittals
Include all requirements listed in RECAP
  SO – Page 83
  MO-1 – Page 89
  MO-2 – Page 97
  MO-3 – Page 108
  Appendix I Assessment – I-21
Include all information, data, etc to allow the reviewer to be able to reproduce all calculations, verify all assumptions, conclusions, etc.

## Slide 200: RECAP Document
To obtain an electronic copy of the Document:
http://www.deq.louisiana.gov/portal/Default.aspx?tabid=1569
To obtain a hard copy of the Document:
http://www.deq.louisiana.gov/portal/LinkClick.aspx?link=planning%2fregs%2ftitle33%2f2007ercform.pdf

## Slide 201: RECAP
Additional information on specific topics pertaining to the interpretation/ implementation of RECAP is available online in the FAQs posted at:
http://www.deq.louisiana.gov/portal/Portals/0/technology/recap/RECAP-2003-FAQs.pdf

## Slide 202: RECAP
RECAP tools are available at:
http://www.deq.louisiana.gov/portal/default.aspx?tabid=1567
Spreadsheet for Appendix H equations
Spreadsheet for Appendix I equations
Domenico Model
Spreadsheet for H-statistic 95%UCL-AM
Copies of RECAP presentations by topic

## Slide 203: Questions?