## Slide 1: Louisiana Department of Environmental Quality Risk Evaluation/Corrective Action Program (RECAP) October 20, 2003

## Slide 2: Advanced RECAP Workshop

## Slide 3: Comparison of Options Getting the most out of RECAP
MO-2
MO-3

## Slide 4: RECAP: Which Option?
SO vs MO-1 vs MO-2 vs MO-3

## Slide 5: What makes sense for your AOI?
   SO  MO-2 or MO-3
  
   MO-1  MO-3
  
   MO-2
  
   MO-3

## Slide 6: SO vs MO-1
Soilni and Soili
Carcinogens: SS = MO-1 RS
Noncarcinogens: SS = MO-1 RS/10
SoilGW
SS: based on groundwater 1 zone
MO-1: site-specific

## Slide 7: SO vs MO-1
Soiles, GWes, GWair
SS: not addressed
MO-1: default RS available

## Slide 8: SO vs MO-1
Advantages of SO:
Quick screen with minimal effort
Site-specific SS based on areal extent of soil source area can be developed
Helps to focus further assessment
Disadvantages of SO:
Cannot tailor assessment to site-specific conditions (GW, DF, etc)
Most conservative, limited option
Frequently leads to higher tier
AOIC based on max detect

## Slide 9: SO vs MO-1
Advantages of MO-1:
Can tailor assessment to site-specific conditions (GW, DF, additivity, etc) with minimal effort
AOIC based on 95%UCL-AM
Addresses more pathways (Soiles, GWes, GWair)
Less conservative screening option
Disadvantages of MO-1:
AOI must be < 0.5 acre option
Requires more effort

## Slide 10: MO-2: When?
Soil: When site-specific EF&T data will  LRS
If AOIC > LRS and LRS is SoilGW or Soilsat (foc)
If AOIC > SoilGW2 or SoilGW3 (DAF)
If AOIC > Soiles or Soil-PEF
If AOIC > Soilni or Soili and COC is VOA (foc)
Other:
If AOIC > Soilni or Soili (NC – site-specific apportionment)
If areal extent of soil AOI > 0.5 acre

## Slide 11: MO-2: When not?
Soil: When site-specific EF&T data will not  LRS
Generally, when LRS is risk-based or otherwise not dependent on EF&T data
  Soili or ni (risk-driven)
  TPH 10,000 ppm cap
  BG

## Slide 12: MO-2: When?
Groundwater: When site-specific EF&T data will  LRS
If CC > MO-1 GW2 or GW 3 (DAF)
If CC > MO-1 GWes
If CC > GWair

## Slide 13: MO-2: When not?
Groundwater: When site-specific EF&T data will not  LRS
Generally, when LRS is risk-based or otherwise not dependent on EF&T data
  GW1
  TPH 10,000 ppm cap
  Watersol
  BG

## Slide 14: MO-3: When?
Soil: When site-specific exposure data or sophisticated EF&T modeling will  LRS
If AOIC > Soili (possibly Soilni)
If AOIC > SoilGW (DAF)
If AOIC > Soiles
If AOIC > Soil-PEF

## Slide 15: MO-3: When?
Groundwater: When site-specific exposure data or sophisticated EF&T modeling will  RS
If CC > GW2 or GW3 (DAF)
If CC > GWes
If CC > GWair
When not?
  GW1
  Watersol
  TPH cap of 10,000 ppm
  BG

## Slide 16: MO-3: When?
Media other than soil and gw impacted
Other exposure pathways present
Sophisticated EF&T analysis warranted
Higher cancer risk level justifiable (Section 2.14.3)

## Slide 17: Comparison of Options
 | SO | MO-1 | MO-2 | MO-3
AOC must meet criteria | Y | Y | Y | N
Media other than soil and GW | N | N | N | Y
Look up tables | Y | Y | N | N
Can use DFs | N | Y | Y | Y
Must ID limiting standard | Y | Y | Y | Y

## Slide 18: Comparison of Options
 | SO | MO-1 | MO-2 | MO-3
Need to account for additivity | N | Y | Y | Y
Soili/ni | Y | Y | Y | Y
SoilGW | Y | Y | Y | Y
Soilsat | (Y) | Y | Y | Y
GW1, 2, and 3 | N | Y | Y | Y

## Slide 19: Comparison of Options
 | SO | MO-1 | MO-2 | MO-3
Watersol | (Y) | Y | Y | Y
Soiles, GWes, GWair | N | Y | Y | Y
SPLP | Y | Y | Y | Y
Site-specific EF&T data | Y/N | N | Y | Y
Site-specific exposure data | N | N | N | Y

## Slide 20: Comparison of Options
 | SO | MO-1 | MO-2 | MO-3
Scenarios other than industrial or residential | N | N | N | Y
Need to ID AOI and COC | (Y) | Y | Y | Y
Max used as AOIC | Y | (Y) | (Y) | (Y)
95%UCL-AM used as AOIC | N | Y | Y | Y

## Slide 21: Comparison of Options
 | SO | MO-1 | MO-2 | MO-3
Must evaluate soil 0-15 and >15 | Y | Y | Y | Y
Must define vertical and horizontal extent | N | Y | Y | Y
Appendix H equations/default inputs | Y | Y | Y | Y
Must present all inputs and calcs | Y | Y | Y | Y

## Slide 22: Comparison of Options
*Department approval required
 | SO | MO-1 | MO-2 | MO-3
Use of other models/equations | N | N | N | Y
Workplan required | N | N | N/Y | Y
Cancer risk > 10-6 | N | N | N | Y*

## Slide 23: Next step?
AOIC > MO-1 Soilsat
  MO-2 (foc)
AOIC > MO-1 Soili
  MO-2 (foc, site-specific apportionment)
  MO-3 (site-specific exposure data)
AOIC > MO-1 Soilni
  MO-2 (foc, site-specific apportionment)
  MO-3 (possible)

## Slide 24: Next step?
AOIC > MO-1 SoilGW
  MO-1 SPLP
  MO-2 (foc; DAF)
  MO-3 (DAF)
AOIC > MO-1 Soiles
  MO-2 (EF&T; additional sampling)
  MO-3 (modeling)

## Slide 25: Next step?
AOIC > MO-2 Soil-PEF
  MO-2 (collect additional EF&T data)
  MO-3 (modeling)
CC > GW1
  Submit CAP
CC > MO-1 GW2 or GW3
  MO-2 (DAF)
  MO-3 (DAF)

## Slide 26: Next step?
CC > MO-1 GWes
  MO-2 (EF&T; additional sampling)
  MO-3 (modeling)
CC > MO-1 GWair
  MO-2 (foc)
  MO-3 (modeling)
Surface water, sediment, biota, etc impacted
  MO-3

## Slide 27
Two fundamental elements of RECAP:
1. Identification of AOI and Calculation of AOIC
2. Identification of the LRS

## Slide 28: Identification of the AOI and Estimation of the AOIC

## Slide 29
Identification of the
Area of Investigation (AOI)

## Slide 30: Identification of the AOI Section 2.6.1
The AOI is the zone contiguous to, and including, impacted media defined vertically and horizontally by the presence of one or more constituents in concentrations that exceed the limiting standard applicable for the option being implemented.

## Slide 31: AOI Concentration
Soil
  Surface Soil: 0 to 15 ft bgs
  Subsurface Soil: > 15 ft bgs

## Slide 32: Identification of the AOI
Identify limiting standard for option
SO → SS
MO-1 → SS
MO-2 → MO-1 RS (Site-specific SS)
MO-3 → MO-2 RS

## Slide 33: Identification of the AOI
Compare limiting standard to concentration detected at each sampling location
Identify each location where the concentration > limiting standard
“Connect the dots” to define the horizontal and vertical boundaries of AOI

## Slide 34: Identification of the AOI LRS = 10 ppm
AOI
B2
16 ppm
B4
< 0.005
B3
32 ppm
B7
<0.005
B11
18 ppm
B5
12 ppm
B6
17 ppm
B9
22 ppm
B8
<0.005
B10
<0.005
B17
<0.005
B12
<0.005
B13
29 ppm
B14
18 ppm
B15
15 ppm
B16
1 ppm
B18
2 ppm
B1
55 ppm
B19
<0.005
B20
2 ppm
B21
1 ppm
B22
2 ppm
B23
<0.005
B24
1 ppm
B25
<0.005
B26
<0.005
B27
<0.005
B28
<0.005
B29
<0.005
B30
<0.005

## Slide 35: Identification of the AOI
15’ bgs
B2
14 ppm
B1
33 ppm
B3
12 ppm
B11
11 ppm
B7
<0.01
B4
<0.01
B5
<0.01
B8
2ppm
B13
13 ppm
B16
4 ppm
B18
<0.01
B14
6 ppm

## Slide 36: Identification of the AOI Tiered Approach
Area > SS
SO: Identify all sampling locations > SS
AOI for MO-1
If all locations < SS  NFA

## Slide 37: Identification of the AOI Tiered Approach
MO-1 AOI
(Area > SS)
MO-1: 1) AOI defined by locations > SS
2) Determine AOIC for AOI
3) Compare to MO-1 LRS, if < LRS  NFA
4) If AOIC > LRS  Id AOI for MO-2
MO-2 AOI
(Area > MO-1 RS)

## Slide 38: Identification of the AOI Tiered Approach
MO-2 AOI
(Area > MO-1 RS)
MO-2: 1) AOI defined by locations > MO-1 LRS
2) Determine AOIC for AOI
3) Compare to MO-2 LRS; if < LRS  NFA
4) If AOIC > LRS  Id AOI for MO-3
MO-3 AOI
(Area > MO-2 RS)

## Slide 39: Identification of the AOI Tiered Approach
Remediate
Area > MO-3 RS
MO-3: 1) AOI defined by locations > MO-2 LRS
2) Determine AOIC for AOI
3) Compare to MO-3 LRS, if < LRS  NFA
4) If AOIC > LRS  Id area to be remediated
MO-3 AOI
(Area > MO-2 RS)

## Slide 40: Identification of the AOI Site-specific SoilSSi/ni
If AOC does not qualify for SO:
Area of impacted soil > 0.5 acre
  all other criteria for SO are met
Develop site-specific SoilSSi or SoilSSni
  site-specific area of impacted soil
  Appendix H

## Slide 41: Identification of the AOI Site-specific SoilSSi/ni
Identify limiting SS
  site-specific SoilSSi or SoilSSni
  Table 1 SoilSSGW
Identify AOI using limiting soil SS
May be re-iterative process

## Slide 42: Identification of the AOI
If only 1 or 2 sampling locations > SS or LRS:
Identification of an AOI is not possible
Options:
  Evaluate under higher tier
  If appropriate, re-sample area
  Remediate impacted area(s)

## Slide 43: Identification of the AOI Based on Land Use
Industrial Soil AOI
Soili
Soilgw
Soilsat
Industrial property
boundary
Residential
AOI
Soilni
(Soilgw)
(Soilsat)

## Slide 44: Identification of the AOI Based on COC
AOI for
COC #2
AOI for COC #1

## Slide 45: Identification of the AOI Single vs Multiple
AOI
AOI
AOI
AOI
Considerations:
Distance
Receptor activity patterns
COC

## Slide 46: Soiles
Enclosed
Structure
Soil to ES AOI
Soili or Soilni
Soilgw
Soilsat
Soil AOI
Soiles

## Slide 47: GWes
Enclosed
Structure
Groundwater AOI
GW to ES AOI
GW1, 2, or 3
Watersol
GWes

## Slide 48: Soil-PEF
Soil AOI
Soili or Soilni
Soilgw
Soilsat
Unpaved
Road
Soil-PEF
AOI

## Slide 49: Estimation of the AOIC

## Slide 50: AOIC
Soil
  Surface Soil AOIC: 0 to 15 ft bgs
    Soilni, Soili, Soiles, Soil-PEF (SoilGW, Soilsat)
  Subsurface Soil AOIC: > 15 ft bgs
    SoilGW, Soilsat
  (Soil AOIC: 0-depth of impact)
    SoilGW, Soilsat

## Slide 51: AOI Concentration Sections 2.8.1 and 2.8.2
AOIC → Lower of 95% UCL-AM and Max
95% UCL-AM
  what is it?
  why is it used?
  other upper bound estimates of mean

## Slide 52: AOI Concentration Sections 2.8.1 and 2.8.2
Soil AOIC
  Based on all data points on or within the AOI
  Includes ND on or within the AOI
  Does not include data points outside the AOI

## Slide 53: AOIC 95% UCL-AM
Determine constituent distribution*
  LogNormal
  Normal
  Non-Normal

## Slide 54: AOIC
Calculate 95%UCL-AM
  RECAP spreadsheet (lognormal only)
    http://www.deq.louisiana.gov/portal/Portals/0/technology/recap/LognormalA5.xls
  ProUCL 4.0
    http://www.epa.gov/nerlesd1/tsc/form.htm

## Slide 55: AOIC
ProUCL and RECAP:
  Log-normal distribution: H-Statistic
  Normal distribution: Student-t Statistic
  Non-normal distribution: ProUCL recommendation
    99%UCL-AM vs 95%UCL-AM

## Slide 56: Identification of the AOI LRS = 10 ppm
AOI
B2
16 ppm
B4
< 0.005
B3
32 ppm
B7
<0.005
B11
18 ppm
B5
12 ppm
B6
17 ppm
B9
22 ppm
B8
<0.005
B10
<0.005
B17
<0.005
B12
<0.005
B13
29 ppm
B14
18 ppm
B15
15 ppm
B16
1 ppm
B18
2 ppm
B1
55 ppm
B19
<0.005
B20
2 ppm
B21
1 ppm
B22
2 ppm
B23
<0.005
B24
1 ppm
B25
<0.005
B26
<0.005
B27
<0.005
B28
<0.005
B29
<0.005
B30
<0.005

## Slide 57: AOI Concentration 95% UCL-AM
Dataset for the upper bound estimate of the mean:
B1 55 ppm B7 0.01 ppm
B2 16 ppm B9 22 ppm
B3 32 ppm B11 18 ppm
B4 0.005 ppm B13 29 ppm
B5 12 ppm B14 18 ppm
B6 17 ppm B15 15 ppm

## Slide 58: ProUCL
ProUCL Output for example AOI:
12 samples
Data are normally distributed
Statistical recommendation is Student’s t UCL of 27.1 ppm
Max concentration is 55 ppm
AOIC = 27.1 ppm

## Slide 59: AOI C
Other considerations:
If max > LRS → calculate 95%UCL-AM BEFORE assessing AOI under higher tier
If dataset is small or has high variability, the 95%UCL-AM > Max
   Use Max Concentration as the AOIC
Nondetects: SQL vs ½ SQL

## Slide 60: AOIC
Background
  Background RS are based on mean values
  AOIC should also be based on the mean not 95%UCL-AM
Other measures
  Surface-weighted average (polygons)
  Volume-weighted average

## Slide 61: Soiles AOIC
Enclosed
Structure
X
X
X
X
X
X
X
X
X
X
X
Soil AOI

## Slide 62: Soiles AOIC
Soili or Soilni
Soilgw
Soilsat
Soil AOI
Soiles
Enclosed
Structure

## Slide 63: GWes AOIC
Enclosed
Structure
X
Groundwater AOI
POC
Flow

## Slide 64: GWes AOIC
Groundwater AOI
GW1, 2, or 3
Watersol
GWes
Enclosed
Structure

## Slide 65: Soil-PEF AOIC
Unpaved
Road
Soil-PEF
AOI
AOIC based on
data points
in this area

## Slide 66: Soil-PEF AOI
Soili-PEF or Soilni- PEF
Soilgw
Soilsat

## Slide 67: Identification of the AOI Remediation Verification
Area Identified for
Remediation
(Area > LRS)
Post-Remediation
AOI

## Slide 68: AOI Concentration
RECAP submittal should:
Identify the standards used to delineate the AOI
Illustrate the boundaries of the AOI
Identify data points used to calculate 95%UCL-AM
Present spreadsheet/output of software
Identify the value to be used as the AOIC for comparison to RS

## Slide 69: Identification of the Limiting RECAP Standard

## Slide 70: Identification of the limiting RECAP Standard
RECAP Standards are developed for:
protection of human health  RS
prevention of cross-media transfer  RS
protection of resource aesthetics  RS
These standards are compared and the lowest is identified as the Limiting Standard

## Slide 71: Identification of the RECAP Standard
The
Limiting Standard
is the standard that is compared to the AOIC or CC

## Slide 72: Management Option 1
Identification and Application of the
Limiting Soil RECAP Standard
Table 2
Appendix H

## Slide 73: Id of the MO-1 Soil LRS Table 2
  Soili (Footnote N)
  Soilni (Footnote N)
  SoilGW1
  SoilGW2 (Footnote x DF2)
  SoilGW3 (Footnote x DF3)
  Soilsat
Limiting RS = lower of these 3 RS
Additivity
See Appendix H
for DF2 and DF3
Applicable to liquids

## Slide 74: Surface Soil 0-15 ft bgs
Surface
AOI
15 feet
Concerns:
1. Soili or Soilni
2. SoilGW
3. Soilsat
4. +/- Soiles

## Slide 75: Id of the MO-1 Limiting Soil RS
Depth of Impact < 15 ft bgs
  0 - depth of impact: lower of the Soili/ni, SoilGW, Soilsat

## Slide 76: Subsurface Soil > 15 ft bgs
Surface
Concerns:
1. SoilGW
2. Soilsat
15 feet
AOI

## Slide 77: Identification of the MO-1 Limiting Soil RS
Depth of Impact > 15 ft bgs
  0 to 15 ft bgs: lower of Soili/ni, SoilGW, Soilsat, (Soiles)
  0 to depth of impact: lower of SoilGW, Soilsat

## Slide 78: MO-1 Soil LRS
Identify the Soilni or Soili and adjust for additivity
Identify the SoilGW and multiply by DF
Identify the Soilsat
Identify the lower of these 3 values → LRS

## Slide 79: Soiles
Identify the Soiles adjust for additivity
Identify the SoilGW and multiply by DF
Identify the Soilsat
Identify the lower of these 3 values → LRS

## Slide 80: Id of the MO-1 Limiting Soil RS Example
Example: Toluene; industrial site; GW3 aquifer; Sd = 5 ft;
distance from source to SW (DW) = 1200 ft
Table 2: Soili = 4800 mg/kg
SoilGW3DW = 120 x DF3 of 173 = 20,760 mg/kg
Soilsat = 520 mg/kg
Limiting RS (LRS) = 520 mg/kg (lower of the 3 RS)

## Slide 81: MO-1 SoilGW DF Appendix H

## Slide 82: Estimation of Sd
Sd = Thickness of impacted groundwater within permeable zone
Un-impacted groundwater
10’
15’
Impacted groundwater
5’
Sd = 5’

## Slide 83: Estimation of Sd
Sd = Thickness of permeable zone if thickness is not known or if the zone is not impacted
Un-impacted groundwater
10’
15’
Sd = 15’

## Slide 84: TPH
If the SoilGW2 x DF2 > 10,000 mg/kg, then default to 10,000 mg/kg
If the SoilGW3 x DF3 > 10,000 mg/kg, then default to 10,000 mg/kg

## Slide 85: Management Option 1
Identification and Application of the
Limiting GW RECAP Standard
Table 3
Appendix H

## Slide 86: MO-1 GW LRS Table 3
  GW1 (Footnote N)
  GW2 (Footnote x DF2)
  GW3 (Footnote x DF3)
  GWair Additivity
  S (Watersol)
Limiting groundwater RS = lower of the 3 RS
Additivity

## Slide 87: GW 1 zone
Identify the GW1
  if applicable, adjust for additivity
Identify the Watersol
If < 15 ft, identify the GWair
  if applicable, adjust for additivity
Identify the lower of these values as the LRS

## Slide 88: GW 2 zone
Identify the GW2
  if applicable, adjust for additivity
  if applicable multiply by DF2
Identify the Watersol
If < 15 ft, identify the GWair
  if applicable, adjust for additivity
Identify the lower of these values as the LRS

## Slide 89: GW 3 zone
Determine if downgradient surface water body is DW or NDW (LAC 33:IX, §1123, Table 3)
Identify the GW3DW or GW3NDW
  if applicable multiply by DF3
Identify the Watersol
If < 15 ft, identify the GWair
  if applicable, adjust for additivity
Identify the lower of these values as the LRS

## Slide 90: GWes
Identify the GW1, GW2 or GW3
  if appropriate, adjust for additivity, apply DF
Identify the GWes
Identify the Watersol
Identify the lower of these values as the LRS

## Slide 91: Id of the MO-1 Limiting GW RS Example
Example: EDC; industrial site; GW3 aquifer; Sd = 7 ft;
distance from source to SW (DW) = 1400 ft
Table 3: GW3DW = 0.00036 mg/l x DF3 of 124 = 0.045 mg/l
Watersol = 8500 mg/l
Limiting RS (LRS) = 0.045 mg/l (lower of the 2 RS)

## Slide 92: MO-1 GW2/GW3 DF Appendix H

## Slide 93: Other considerations
If the GW3 X DF3 < GW2, then manage COC using GW2 x DF2

## Slide 94: Management Option 2
Identification and Application of the
Limiting RECAP Standard
Appendix H

## Slide 95: MO-2 LRS
No look up table
RS are developed using site-specific EF&T
In absence of SS EF&T, use defaults in App H
Identification of LRS same as for MO-1

## Slide 96: MO-3 LRS
No look up table
RS are developed using site-specific EF&T and exposure data
In absence of SS EF&T and/or exposure data, use defaults in App H
Identification of LRS same as for MO-1

## Slide 97: RECAP
Alternatives to Applying
RECAP Standards
Notes: I’d like to give you a brief overview of the RECAP Program and then Dr. Sutherlin will present a more detailed review.

## Slide 98: RECAP
Soiles  Soil gas or indoor air sampling (MO-2 and 3)
GWes  Soil gas or indoor air sampling (MO-2 and 3)
SoilGW  SPLP (all options)
Notes: I’d like to give you a brief overview of the RECAP Program and then Dr. Sutherlin will present a more detailed review.

## Slide 99: Soil to Groundwater Pathway SPLP Data
Where should SPLP samples be collected?
How is the SPLP data used to evaluate the soil to gw pathway?
  SoilGW1: Compare SPLP to GW1 x DFSummers
  SoilGW2: Compare SPLP to GW2 x DFSummers x DF2
  SoilGW3: Compare SPLP to GW3 x DFSummers x DF3

## Slide 100: Soil to Groundwater Pathway SPLP Data
  If SPLP <, then screen out soil to GW pathway
  If SPLP >, then delineate area of concern
  SPLP vs TCLP
  SPLP vs LRS
    Omit SoilGW RS from identification of LRS

## Slide 101: Other considerations
RS based on:
SQL
Background
Ceiling value

## Slide 102: Calculation of Screening Standards and RECAP Standards

## Slide 103: RECAP Spreadsheet
http://www.deq.louisiana.gov/portal/default.aspx?tabid=1567

## Slide 104: SS or RS for COC not in RECAP
Example: isopropylbenzene (cumene) CAS 98-82-2
RECAP spreadsheet:
  http://www.deq.louisiana.gov/portal/default.aspx?tabid=1567
IRIS: toxicity values
  http://www.epa.gov/iris/subst/0306.htm
  Oral RfD = 1E-01 mg/kg-d; target: kidney
  RfC = 4E-01 mg/m3; target: kidney, adrenal gland
  Inhalation RfD = 4E-01 mg/m3 x 20m3/day/70 kg = 1.1E-01 mg/kg-d
Chemical/physical data
  Molecular weight, Koc, HLC, Da, Dw, and solubility

## Slide 105: SS or RS for COC not in RECAP
Example: isopropylbenzene (cumene) CAS 98-82-2
For MO-1 RS, click on tabs for each RS
For SS, divide the risk-based SS based on noncarcinogenic effects by 10.
  Soili ÷10 = SoilSSi
  Soilni ÷ 10 = SoilSSni
  GW1 ÷ 10 = GWSS

## Slide 106: Site-Specific Soil SS
Soilni or Soili
  source area
  Q/C for VF
    Spreadsheet: soil properties and Q/C tab
    length of source at the water table
    width of the impacted area perpendicular to gw flow
    site-specific source area
  Example: Benzene Soili
Site size | 148*148 | 209*209 | 295*295 | 467*467 | 660*660 | 1143*1143
Site size ft2 | 21,904 | 43,681 | 87,025 | 218,089 | 435,600 | 1,306,449
Site size | 0.5 acre | 1 acre | 2 acre | 5 acre | 10 acre | 30 acre
Soili mg/kg | 3.1 | 2.7 | 2.4 | 2.1 | 1.9 | 1.6

## Slide 107: MO-2 Soil RECAP Standards Use of Site-Specific Data
Soilni or Soili (VF)
  source area; water-filled soil porosity; dry soil bulk density; foc
Soilni-PEF or Soili-PEF
  source area; veg cover; windspeed
SoilGW1, SoilGW2, or SoilGW3
  dry soil bulk density; water-filled soil porosity; foc; soil particle density

## Slide 108: MO-2 Soil RECAP Standards Use of Site-Specific Data
DFSummers
  volumetric flow rate of infiltration; volumetric flow rate of groundwater; infiltration rate; width of impacted area; length of impacted area; hydraulic gradient; hydraulic conductivity; thickness of mixing zone; soil concentration; dry bulk density; total soil porosity; water filled soil porosity; foc

## Slide 109: MO-2 Soil RECAP Standards Use of Site-Specific Data
DAFDomenico
  source width; hydraulic gradient; hydraulic conductivity; soil porosity; degradation rate; retardation factor; distance from source; source thickness (Sd)

## Slide 110: MO-2 Soil RECAP Standards Use of Site-Specific Data
Soiles
  dry soil bulk density; depth to subsurface soils; water-filled soil porosity; air exchange rate; volume/ infiltration area ratio; foundation thickness; foc; area fraction of cracks in foundation; air-filled soil porosity; total soil porosity; dry soil bulk density; soil particle density; volumetric air content in foundation cracks; volumetric water content in foundation
Soilsat
  dry soil bulk density; water-filled soil porosity; soil particle density, foc

## Slide 111: MO-2 Groundwater RS Use of Site-Specific EF&T Data
GW1, GW2, GW3 - Not Applicable
DAFDomenico
  source width; hydraulic gradient; hydraulic conductivity; soil porosity; degradation rate; retardation factor; distance from source; source thickness

## Slide 112: MO-2 Groundwater RS Use of Site-Specific EF&T Data
GWes
  depth to groundwater; air exchange rate; volume/infiltration area ratio; foundation thickness; areal fraction of cracks in foundation; thickness of capillary fringe; thickness of vadose zone; volumetric air content in foundation cracks; volumetric water content in foundation cracks; total porosity; dry bulk density; particle density; volumetric air content in capillary fringe soils; volumetric water content in capillary fringe soils; water filled soil porosity

## Slide 113: MO-2 Groundwater RS Use of Site-Specific EF&T Data
GWair
  depth to groundwater; wind speed; width of source area; ambient air mixing zone height; thickness of capillary fringe; thickness of vadose zone; volumetric air content in capillary fringe soils; volumetric water content in capillary fringe soils; dry bulk density; water filled soil porosity; total porosity; particle density

## Slide 114: Fraction of organic carbon (foc)
ASTM D2974 Heat Loss on Ignition
foc = Percent organic matter/174
SW-846 Method 9060 Total Organic Carbon
foc = TOC (mg/kg)/1E-06

## Slide 115: Fraction of organic carbon (foc)
Example: Benzene, site-specific foc= 0.02
Spreadsheet, soil properties and Q/C tab, replace default 0.006 with 0.02
Mg/kg | Soilni | Soili | SoilGW1 SoilGW2 | SoilGW3DW | SoilGW3NDW | Soilsat | Soilesni | Soilesi
Default | 0.79 | 1.6 | 0.011 | 0.0023 | 0.027 | 900 | 1.0 | 2.5
Site-specific | 1.3 | 2.6 | 0.029 | 0.0063 | 0.071 | 2400 | 2.7 | 6.7

## Slide 116: Toxicity Assessment

## Slide 117: Toxicity Assessment
Dose Response  Toxicity Values
Toxicity Values include:
  Reference doses (RfD) and Reference concentrations (RfC) which are used to assess noncarcinogenic effects (threshold effects)
  Cancer slope factors (CSF) and cancer unit risks which are used to assess carcinogenic effects (non-threshold effects)

## Slide 118: IRIS
Integrated Risk Information System
http://www.epa.gov/iris/subst/index.html

## Slide 119: Toxicity Assessment
Hierarchy for Toxicity Values - RECAP
IRIS
EPA provisional values - NCEA
HEAST
Withdrawn from IRIS or Heast
Other EPA source or non-EPA-source

## Slide 120: Toxicity Assessment
Hierarchy for Toxicity Values
Memorandum - OSWER Directive 9285.7-53 EPA Dec 5, 2003
IRIS
EPA provisional peer reviewed toxicity values (PPRTV)
Other toxicity values (EPA and non-EPA)
  HEAST
  Withdrawn from IRIS or HEAST
  ATSDR MRL

## Slide 121: Toxicity Assessment
Toxicity Values – bottom line
IRIS
EPA Region 6
  Human Health Medium-Specific Screening Levels
  http://www.epa.gov/earth1r6/6pd/rcra_c/pd-n/screen.htm
  PPRTVs, HEAST, other EPA sources, withdrawn toxicity values

## Slide 122: Reference Dose/Reference Concentration
An estimate of a daily exposure level for the human population (including sensitive subpopulations) that is likely to be without an appreciable risk of deleterious health effects during a lifetime.
Noncarcinogenic health effects

## Slide 123: Reference Dose/Reference Concentration
Noncarcinogenic = Threshold effects
Protective for chronic exposure (7-70 yr)
Chemical, route, duration-specific
Target organ/Critical effect

## Slide 124: Reference Dose/Reference Concentration
RfDo - oral exposure; mg/kg-d
RfC - inhalation exposure; mg/m3
RfDi = RfC x 20 m3/d  70 kg
Dermal RfD = NA (use oral value)
  RAGS-E

## Slide 125: Toxicity Assessment
Development of a Reference Dose:
Concept of threshold effects
RfD = NOAEL/UF x MF
UF: 10 - intraspecies
  10 - interspecies
  10 - study duration
  10 - LOAEL
MF: > 0 to 10
Target or effect observed at LOAEL = target/effect the RFD serves to protect

## Slide 126: Toxicity Assessment
Development of a Reference Dose for Chemical Z:
2 yr Rat study - gavage
3 Rx Groups: 100, 150, and 250 mg/kg-d
Results of study:
100 - no adverse effects
150 -  kidney function; liver hyperplasia
250 -  kidney function/failure; 20% mortality; lipid infilt.liver
RfDo = NOAEL/UF
RfDo = 100/10 x 10 = 1 mg/kg-d
Critical effects: kidney and liver toxicity

## Slide 127: Threshold Dose-Response Curve Noncarcinogens
UF x MF
RfD
NOAEL
Response
Dose (mg/kg-d)

## Slide 128: Slope Factor/Inhalation Unit Risk
Defines quantitatively the relationship between dose and response for nonthreshold effects (carcinogenic effects = cancer)
The slope factor is an upper bound estimate of the probability of a response per unit intake of chemical over a lifetime
Chemical and route-specific

## Slide 129: Slope Factor/Inhalation Unit Risk
SFo is expressed in units of risk per mg/kg-d
Inhalation unit risk is expressed in units of risk per ug/m3
Inhalation unit risk  inhalation SF
  SFi = Unit risk X 70 kg/20 m3/d x CF
No Dermal SF; use oral.

## Slide 130: Slope Factor/Inhalation Unit Risk
No target organ/critical effect identified with regard to additivity
Weight of evidence classifications
  Group A Human carcinogen
  Group B1 Probable human carcinogen, limited human data available
  Group B2 Probable human carcinogen, sufficient evidence in animals and inadequate or no evidence in humans
  Group C Possible human carcinogen
  Group D Not classifiable as to human carcinogenicity
  Group E Evidence of noncarcinogenicity for humans

## Slide 131: Toxicity Assessment
Development of a Slope Factor:
Concept of non-threshold effects
Model used to extrapolate from high dose to low dose
Slope of the dose-response curve represents response per unit of chemical intake

## Slide 132: Non-threshold Dose-Response Curve Carcinogens
?
10 0
10-1
10-2
10-3
10-4
10-5
10-6
Dose
(mg/kg-d)
Probability of Response

## Slide 133: Non-threshold Dose-Response Curve Carcinogens
10-1
10-2
10-3
10-4
10-5
10-6
10 0
Probability of Response
Dose
mg/kg-d

## Slide 134: Slope Factors
Slope Factor ranges
  Benzene
    SFo = 1.5E-02 to 5.5E-02 per mg/kg-d
    Air Unit Risk = 2.2E-06 to 7.8E-06 per ug/m3
  TCE
  1,2-dibromoethane
  No EPA guidance

## Slide 135: Slope Factors
Slope Factors:
Exposure duration
  vinyl chloride
Persistence/exposure pathway
  PCB
Relative potency factors
  PAH
Toxicity Equivalent Factors
  PCDD/PCDF

## Slide 136: Toxicity Assessment
If an EPA toxicity value is not available:
Route-to-route extrapolation
  Oral for inhalation (organics only)
  EPA Regions III, VI, and IX
  Inhalation for oral (organics only)
  EPA Regions VI and IX
  Not appropriate if target/critical effect is a portal of entry effect

## Slide 137: Toxicity Assessment
  Example: Phenol, citation from IRIS
  I.B.1. Inhalation RfC Summary
  No adequate inhalation exposure studies exist from which an inhalation RfC may be derived. A route-to-route extrapolation is not appropriate, because phenol can be a direct contact irritant, and so portal-of-entry effects are a potential concern.

## Slide 138: Toxicity Assessment
If an EPA toxicity value is not available:
Surrogate approach
Development of a toxicity value from literature
Equivalent values - ATSDR Minimal Risk Levels
Qualitative evaluation 

## Slide 139: Toxicity Assessment
Surrogate Approach:
Structure-activity relationships
Noncarcinogenic/carcinogenic effects
Target organ/critical effect
Toxicokinetics

## Slide 140: Surrogate Approach
anthracene
phenanthrene
Benz[a]anthracene
chrysene

## Slide 141: No toxicity values  Call LDEQ Toxicological Services Division 219-3421 Before completing RECAP Assessment

## Slide 142: Revised Toxicity Values
If a Toxicity Value has been revised since 2003, the revised values should be used for:
  MO-2 RS
  MO-3 RS

## Slide 143: Additivity

## Slide 144: Addressing Exposure to Multiple Constituents that Elicit Noncarcinogenic Effects on the Same Target Organ/System

## Slide 145: Additivity - Noncarcinogens
No risk “range”
For the assessment of noncarcinogenic health effects, exposure is acceptable when < RfD
RS are based on a THQ = 1.0  acceptable exposure
  Hazard quotient = Exposure/RfD = AOIC/RS

## Slide 146: Risk-based RS
RS address exposure via multiple pathways
    Soil: ingestion, inhalation, and dermal contact
    Drinking water: ingestion and inhalation
Represent an acceptable exposure level for exposure to a single chemical via a single medium (THQ =1)
Do not address additivity due to exposure to multiple chemicals or multiple exposure media
Multiple constituents or impacted media could result in a total hazard index greater than 1.0

## Slide 147: Additivity - Noncarcinogens
The hazard index is defined as the sum of more than one hazard quotient for multiple noncarcinogenic constituents and exposure pathways:
HI = [HQ1) + (HQ2) + … + (HQi)
where:
HI = Hazard Index for target organ/critical effect
HQi = HQ for the ith COC
HI < 1.0 for all target organs/critical effects identified for noncarcinogenic COC

## Slide 148: Risk-based RS
Risk-based RS must be adjusted to account for potential additive effects
  Soilni, Soili, Soiles
  GW1, GW2, GWes, GWair
Not applicable to SoilGW, Soilsat, GW3, Watersol, background levels, quantitation limits, MCLs, ceiling values

## Slide 149: Additivity - Noncarcinogens
Additivity applicable only to constituents that have same critical effect/target organ
Risk-based standards for constituents that produce noncarcinogenic effects on the same target organ/critical effect must be modified to account for additive effects
Constituents are grouped by critical effect (target organ/system) listed as the basis for the RfD and RfC

## Slide 150: Target organ/critical effect
Example from IRIS - Toluene
I.A.1. Oral RfD Summary
Critical Effect Experimental Doses *UF RfD
Increased kidney weight BMDL: 238 mg/kg-day 3000 0.08 mg/kg-day BMD: 431 mg/kg-day
13-week gavage study in rats (NTP, 1990)
I.B.1. Inhalation RfC Summary
Critical Effect Experimental Doses *UF RfC
Neurological effects NOAEL (average): 10 5 mg/m3
in occupationally-exposed 34 ppm (128 mg/m3) Workers NOAEL (ADJ): 46 mg/m3
Multiple human studies

## Slide 151: Appendix G
Additivity examples
Table G-1 target organs/critical effects for MO-1 RS
If a toxicity value and target organ have been revised since 2003, the revised value and target should be used for MO-2 and MO-3 but Table G-1 should be used for MO-1.

## Slide 152: Additivity - Noncarcinogens
MO-1: If > 1 NC constituent has same critical effect, risk-based standards are divided by the number of constituents having the same target
MO-2 and MO-3: Risk-based standards can be modified based on site-specific conditions

## Slide 153: MO-1: Accounting for Additivity
Modification of risk-based MO-1 RS:
  group noncarcinogenic chemicals by target organ/critical effect

## Slide 154: MO-1: Accounting for Additivity
1. Identify the target organ/critical effect for each noncarcinogenic chemical (RfD)
  http://www.epa.gov/iris/subst/index.html
2. Group the chemicals by target organ/critical effect
3. Divide the RS by the number of chemicals affecting the same target organ

## Slide 155: MO-1: Accounting for Additivity Example
Chemical Target Organ RS Adjusted RS
A kidney 24 8
B kidney, liver 15 5
C CNS 10
D kidney 60 20
Divide the RS for A, B, and D by 3 (kidney)
(Same as calculating a RS using a THQ of 0.33)

## Slide 156: MO-2: Methods for Accounting for Additivity
Modification of risk-based MO-2 RS:
  group by target organ/critical effect
  site-specific apportionment of RS or THQ
  calculation of a total HI for each target organ

## Slide 157: MO-2: Additivity Example: Site-specific apportionment
COC Target THQRS THQRS THQRS
A kidney 1.0 2 0.33 0.67 0.8 1.6
B kidney 1.0 90 0.33 30 0.1 9
C kidney 1.0 120 0.33 40 0.1 12
Total HI 1.0 1.0

## Slide 158: MO-2 Additivity Example: Calculation of a THI for Each Target Organ
THIkidney = AOICA/RSA + AOICB/RSB +AOICc/RSc
where:
AOIC = exposure concentration
RS = RECAP Standard
THIkidney = 1/1.6 + 0.5/9 + 3/12 = 0.93
THI must be < 1.0

## Slide 159: Additivity Exposure to Multiple Media
If there is exposure to chemicals via more than one medium, then RS must be modified to account for additivity
Applicable only to MO-2 and MO-3
MO-2 Example: a receptor is being exposed to chemicals via drinking water (GW1 or GW2) and soil

## Slide 160: Additivity - Noncarcinogens
Example: A release of solvents occurred at a petroleum refinery and the COC migrated offsite to an adjacent residential area.
Site investigation data revealed:
Benzene, toluene, ethylbenzene and xylene in soil
Benzene, toluene and xylene in groundwater

## Slide 161: Additivity - Noncarcinogens
Exposure assessment revealed:
The receptors are being exposed to both contaminated soil and contaminated groundwater

## Slide 162: Additivity - Noncarcinogens
1.Adjust for exposure to multiple constituents
  A. Identify the critical effect/target organs (IRIS)
  B. Group the constituents according to the critical effect(s)/target organ(s)
  C. Adjust Standards to account for additivity
2. Adjust for exposure to multiple media

## Slide 163: Additivity - Noncarcinogens
1A.Identify the critical effect/target organs (IRIS) and group the constituents according to the critical effect(s)/target organ(s):
Toluene: liver, kidney, and neurological effects
Ethylbenzene: liver, kidney, and developmental toxicity
Xylene: central nervous system (CNS), decreased body weight, and increased mortality
Benzene is a carcinogen so it is not adjusted for additivity.

## Slide 164: Additivity - Noncarcinogens
1B. Summarize by critical effect/target organ:
  (2) Kidney: toluene, ethylbenzene
  (2) Liver: toluene, ethylbenzene
  (1) CNS/hyperactivity: xylene
  (1) CNS/decreased concentration: toluene
  (1) Body weight change: xylene
  (1) Increased mortality: xylene

## Slide 165: Additivity - Noncarcinogens
1C. Adjust the risk-based levels to account for cumulative effects for each target organ/system:
For toluene, ethylbenzene, the risk-based standards for soil should be divided by 2 to account for additive effects to the liver and the kidney
For xylene, the risk-based standard for soil does not need to be adjusted to account for additivity because there are no other constituents present in the soil affect body weight, produce an increase in mortality, or produce CNS effects

## Slide 166: Additivity - Noncarcinogens
2.Adjust for exposure to more than one medium
  The risk-based levels for soil for toluene and xylene should be adjusted to account for additive effects by dividing the risk based standard by 2.
  The risk-based levels for groundwater for toluene and xylene should be adjusted to account for additive effects by dividing the risk-based standard by 2.

## Slide 167: Additivity: GW1 and GW2
Include all NC COC when identifying targets
If no current exposure:
  Adjust GW1 or GW2 RS based on NC effects
  Do not adjust GW1 or GW2 RS based on MCL

## Slide 168: Additivity: GW1 and GW2
If exposure is occurring:
  Adjust GW1 or GW2 RS based on NC effects
  For GW1 or GW2 RS based on MCL:
  1. Calculate GW1 or GW2 RS for NC effects
  (Appendix H)
  2. Adjust RS to account for additivity

## Slide 169: Enclosed Structure – Soil and GW Additivity Example
Soil: Toluene (liver, kidney, CNS)
Ethylbenzene (liver, kidney, fetal)
Hexachloroethane (kidney)
GW: Chlorobenzene (liver)
Fluoranthene (kidney, liver, hemat.)
Hexachloroethane (kidney)

## Slide 170: Enclosed Structure – Soil and GW Additivity Example
What is the exposure medium?
  Indoor Air
What are the COC for indoor air?
  Volatile COC (HLC > 1E-05 atm-m3/mol and mw < 200 g/mol)
    Toluene (liver, kidney, CNS)
    Ethylbenzene (liver, kidney, fetal)
    Chlorobenzene (liver)

## Slide 171: Enclosed Structure – Soil and GW Additivity Example
Based on additivity to the liver:
Divide the Soiles and GWes for toluene, ethylbenzene, and chlorobenzene by 3

## Slide 172: Additivity - Carcinogens
Target risk level of 10-6 for individual constituents and media
Multiple COC and pathways result in cumulative risks within the 10-4 to 10-6 risk range
Therefore, not necessary to modify the standards to account for exposure to multiple carcinogens or multiple impacted media

## Slide 173: RECAP
Total Petroleum Hydrocarbons
Appendix D
Notes: I’d like to give you a brief overview of the RECAP Program and then Dr. Sutherlin will present a more detailed review.

## Slide 174: TPH Fraction and Indicator Method
Petroleum hydrocarbon releases are assessed based on the identification and quantitation of
indicator compounds and hydrocarbon fractions

## Slide 175: COC for Petroleum Releases Table D-1 Page D-TPH-5
Total Petroleum Hydrocarbons
TPH Fraction and Indicator Compound Approach
http://www.aehs.com/publications/catalog/tph.htm
Indicator compounds may include:
  BTEX
  PAHs
  Metals
  Additives

## Slide 176: Hydrocarbon Fractions Table D-1 Page D-TPH-5
Dependent on type of release
Hydrocarbon fractions include:
  Aliphatics Aromatics
  C>6 – C8 C>8 – C10
  C>8 – C10 C>10 – C12
  C>10 – C12 C>12 – C16
  C>12 – C16 C>16 – C21
  C>16 – C35 C>21 – C35
  C>35 C>35

## Slide 177: TPH Mixtures TPH-G, TPH-D, and TPH-O
TPH-GRO = C6 - C10
TPH- DRO = C10 - C28
TPH-ORO = C>28
Other mixtures

## Slide 178: How were the RS for TPH-GRO, DRO, and ORO derived?
Example: Soilni for TPH-DRO (C10 – C28)
Aliphatics C>8-C10 1200
Aliphatics C>10-C12 2300
Aliphatics C>12-C16 3700
Aliphatics C>16-C35 10,000
Aromatics C>8-C10 650
Aromatics C>10-C12 1200
Aromatics C>12-C16 1800
Aromatics C>16-C21 1500
Aromatics C>21-C35 1800

## Slide 179: TPH
TPH Analytical methods
  TPH - 8015B, Texas 1005
  Fractions – Texas 1006, MDEP VPH/EPH
  PAH – 8310 or 8270
  C>35
  Forensic Fingerprinting – TPH, PAH
  Have both 8015 data and fractionation data but results differ
Table D-1 Identifies COC for various releases
  If the type of release is not in Table D-1 contact LDEQ for COC

## Slide 180: TPH
Table D-2 P/C Properties of fractions
Table D-3 RfD and target organs/critical effects
  TPHCWG; not in IRIS
Table D-4 Critical effects/targets for all petroleum COC
Aesthetic cap of 10,000 ppm

## Slide 181: Additivity and TPH

## Slide 182: Additivity: TPH
Additivity - TPH RS based on 10,000 cap
  Do not adjust 10,000 cap
  Identify risk-based value in Appendix H worksheets
  Adjust risk-based RS to account for additive effects
  If adjusted risk-based RS < 10,000, use risk-based RS
  If adjusted risk-based RS > 10,000, use 10,000 cap

## Slide 183: Additivity: TPH Fractions
Aliphatics C>6-C8
Aliphatics C>8-C16 (C>8-C10, C>10-C12, C>12-C16)
Aliphatics C>16-C35
Aromatics C>8-C16 (C>8-C10, C>10-C12, C>12-C16)
Aromatics C>16-C35

## Slide 184: Additivity: TPH Fractions Example 1
Soil: ethylbenzene, aliphatics C>8-C10, C>10-C12, C>12-C16
Id of targets:
  ethylbenzene: liver, kidney, developmental
  aliphatics C>8-C10: liver, hematological system
  aliphatics C>10-C12: liver, hematological system
  aliphatics C>12-C16 : liver, hematological system
Additivity - Liver: ethylbenzene and aliphatics C>8-C16
Adjustment factor: 2 NOT 4
C>8-C16

## Slide 185: Additivity: TPH Fractions Example 1 (cont’d)
Adjustment of MO-1 Soilni:
  ethylbenzene: 1600/2 = 800 mg/kg
  aliphatics C>8-C10: 1200/2 = 600 mg/kg
  aliphatics C>10-C12: 2300/2 = 1150 mg/kg
  aliphatics C>12-C16 : 3700/2 = 1850 mg/kg

## Slide 186: TPH Additivity Example 2
Gasoline release to non-industrial soil
Table D-1: BTEX, aliphatics C>6-C8, C>8-C10, aromatics C>8-C10

## Slide 187: MO-1 Additivity Example 2: Soil Gasoline release
COC MO-1 Soilni Target Organ/Effect
benzene C ---
ethylbenzene 1600 liver, kidney, develop.
toluene 680 liver, kid., CNS, nas.epi.
xylene 180 activity, bw,mort.
aliphatics C6-8 12,000 kidney
aliphatics C8-10 1200 liver, hematol. sys.
aromatics C8-10 650 bw

## Slide 188: MO-1 Additivity Example 2: Soil Gasoline release
Summarize by target organ:
(3) liver: ethylbenzene, toluene, aliphatics C8-10
(3) kidney: ethylbenzene, toluene, aliphatics C6-8
(1) developmental: ethylbenzene
(1) CNS: toluene
(1) nasal epithelium: toluene
(1) hyperactivity: xylene
(2) bw: xylene, aromatics C8-10
(1) mortality: xylene
(1) hematological system: aliphatics C8-10

## Slide 189: MO-1 Additivity Example 2: Soil Gasoline release
COC Adjusted MO-1 Soilni
benzene C
ethylbenzene 1600  3 = 533 (liver)
toluene 680  3 = 227 (liver)
xylene 180  2 = 90 (bw)
aliphatics C6-8 12,000  3 = 4000 (kidney)
aliphatics C8-10 1200  3 = 400 (liver)
aromatics C8-10 650  2 = 325 (bw)

## Slide 190: MO-1 Additivity Example 2: Soil Gasoline release
Identification of the limiting soil RS:
COC Soilni SoilGWDW* Soilsat
benzene 1.5 4.8 900
ethylbenzene 533 29,040 230
toluene 227 52,800 520
xylene 90 79,200 150
aliphatics C6-8 4,000 10,000 NA
aliphatics C8-10 400 10,000 NA
aromatics C8-10 325 10,000 NA
*based on a DF3 of 440

## Slide 191: TPH Additivity Example 3
Gasoline release to GW1
No current exposure
Table D-1: BTEX, aliphatics C>6-C8, C>8-C10, aromatics C>8-C10

## Slide 192: MO-1 Additivity Example 3: GW Gasoline release
COC MO-1 GW1 Target Organ/Effect
benzene C ---
ethylbenzene MCL liver, kidney, develop.
toluene MCL liver, kid., CNS, nas.epi.
xylene MCL activity, bw, mortality
aliphatics C6-8 32 kidney
aliphatics C8-10 1.3 liver, hematol. sys.
aromatics C8-10 0.34 bw

## Slide 193: MO-1 Additivity Example 3: GW Gasoline release
Summarize by target organ:
(3) liver: ethylbenzene, toluene, aliphatics C8-10
(3) kidney: ethylbenzene, toluene, aliphatics C6-8
(1) CNS: xylene
(2) bw: xylene, aromatics C8-10
(1) mortality: xylene
(1) hematological system: aliphatics C8-10

## Slide 194: MO-1 Additivity Example 3: GW Gasoline release
COC Adjusted MO-1 GW1
benzene C
ethylbenzene MCL
toluene MCL
xylene MCL
aliphatics C6-8 32  3 = 11 (kidney)
aliphatics C8-10 1.3  3 = 0.43 (liver) aromatics C8-10 0.34  2 = 0.17 (bw)

## Slide 195: MO-1 Additivity Example 3: GW Gasoline release
Identification of the limiting GW RS:
COC GW1 Watersol
benzene 0.005 1800
ethylbenzene 0.7 170
toluene 1 530
xylene 10 160
aliphatics C6-8 11 NA
aliphatics C8-10 0.43 NA
aromatics C8-10 0.17 NA

## Slide 196: Example 4 Site-specific Apportionment
Soil data:
COC | AOIC
Ethylbenzene | 610
Toulene | 1150
TPH-GRO | 3500
COC | Target organ/critical effect
Ethylbenzene | Liver, kidney, fetal
Toulene | Liver, kidney, CNS, nasal cavity
TPH-GRO | Liver, kidney, hematological system, ↓ bw

## Slide 197: Example 4 Site-specific Apportionment
Multiply the Soili by the site-specific target hazard quotient to adjust for additivity.
The target hazard quotient may be subdivided any way you like just as long as the THI for the COC < 1.0.
In this example, the total acceptable exposure to the kidney and liver is apportioned on a site-specific basis: 5% for ethylbenzene, 25% for toluene, and 70% for TPH-G.
COC | Soili | Site-specific THQ to adjust for additivity | Final Soili
Ethylbenzene | 13,000 | 0.05 | 650
Toulene | 4700 | 0.25 | 1175
TPH-GRO | 5100 | 0.7 | 3570
 |  | THI = 1.0 | 

## Slide 198: Example 4 Site-specific Apportionment
Multiply the Soili by the site-specific target hazard quotient to adjust for additivity.
The target hazard quotient may be subdivided any way you like just as long as the THI for the COC < 1.0.
In this example, the total acceptable exposure to the kidney and liver is apportioned on a site-specific basis: 5% for ethylbenzene, 25% for toluene, and 70% for TPH-G.
COC | Final Soili | AOIC | Exceeds?
Ethylbenzene | 650 | 610 | No
Toulene | 1175 | 1150 | No
TPH-GRO | 3570 | 3500 | No

## Slide 199: Example 4 Site-specific Apportionment
Check:
THI = AOICE/RSE + AOICT/RST + AOICG/RSG
THI = 610/13,000 + 1,150/4700 + 3,500/5100 = 0.98 < 1.0

## Slide 200: RECAP
A Site-Specific MO-2 RECAP Evaluation for Typical UST Sites
Appendix I
Notes: I’d like to give you a brief overview of the RECAP Program and then Dr. Sutherlin will present a more detailed review.

## Slide 201: Appendix I
MO-2 assessment for typical UST
Soili, Soilni, SoilGW, Soilsat
GW1, GW2, GW3, Watersol
Soiles and GWes can be addressed under MO-2 assessment
GWair can be addressed under MO-2 assessment
16 Category Tables for RS

## Slide 202: Appendix I
Site-specific data
Foc - fraction of organic carbon
Source area
  Soil in vadose zone with COC > MO-1 RS
  Use boring logs to define
  = L x Sw
  L = source length = longest length of source area parallel to gw flow
  Sw = source width = longest length of source area perpendicular to gw flow

## Slide 203: Figure H-1: Schematic Description of Domenico’s Model

## Slide 204: Appendix I

## Slide 205: Appendix I
Site-specific data (cont’d)
Sd
  estimated at downgradient L boundary
Conveyence notice
  Only required when the AOIC > Soilni
  Not required when soil AOIC > other RS
  Concrete cover does not negate requirement for notice
  Required for GW 2 when CC > RS (w/o DF2) within property boundary

## Slide 206: Appendix I
Vapor Intrusion Pathway
  Screen under MO-1
  Develop site-specific MO-2 RS
  Soil Gas Assessment
    Table H5*alpha (Ca x 100)
    Refer to FAQ for specifics of sampling protocol
  Indoor air sampling
  Soil and GW at depth < 15 ft bgs
  VOA = HLC > 1E-05 atm-m3/mol and MW < 200 g/mol

## Slide 207: Appendix I
95%UCL-AM concentration
  ProUCL
  multiple sampling events
  post-remediation
    Include all confirmation sample results and remaining site investigation results within the boundaries of the original AOI
    Include all data points that are representative of current site conditions

## Slide 208: Appendix I
GW3 POE
Identification of AOI – horizontal and vertical extent
Use of SPLP data
Groundwater classification
  DOTD well survey
RS for TPH fractions
Arsenic
    State background level
      AOIC based on mean not 95%UCL-AM
    site-specific background

## Slide 209: Non-Traditional Parameters

## Slide 210: Appendix D
Chlorides, sulfates, pH, etc.
Evaluation dependent on professional judgement
MO-2 or MO-3
Protection of health, ecological receptors, livestock, crops, and vegetation
Prevent migration and cross-media transfer
Protect beneficial uses of medium/aesthetics
Protect structures

## Slide 211: Appendix D
Identify any and all ARARs
Identify tolerance levels for native veg/crops
Consider solubility, soil saturation
Odor and taste thresholds
Visual considerations

## Slide 212: Appendix D
Example: Chloride in groundwater 3 zone
Refer to LAC 33:IX, §1123, Table 3 to identify the criterion for chloride in downgradient SW body as the RS
Apply DF3
Compare to CC at the POC

## Slide 213: Appendix D
Example: Low pH in groundwater 3 zone
Refer to LAC 33:IX, §1123, Table 3 to identify the criterion for pH in downgradient SW body as the RS
Convert RS from pH units to [H+]
Apply DF3; convert RS [H+] to pH units
Compare to pH at the POC
pH = -log10[H+]

## Slide 214: Appendix D
Example: Drinking water standard for aluminum for livestock
Literature review to identify toxicity info
  Maximum tolerable concentration in diet is 1000 mg/kg
  Cow eats 9.5 kg food/day
  1000 mg Al/kg food x 9.5 kg food = 9500 mg Al/day
  9500 mg Al/day ÷ body weight 454 kg = 21mg/kg-d
  RfD = 21 mg/kg-d

## Slide 215: Appendix D
Example: Drinking water standard for aluminum for livestock
Drinking water standard = RfD x BW
IRw
= 21 mg/kg-d x 454 kg
45 l/day
= 211 mg/l = RS
3. Compare RS to Al concentration at POC

## Slide 216: Data Issues

## Slide 217: Data Collection Issues
Analyte list
  Site-related COCs
  TICs
Sample Quantitation Limits
  SQL vs limiting RS
Blank Samples
Analytical Method
  ex) PAHs

## Slide 218: Data Evaluation/Data Usability
RECAP Section 2.5

## Slide 219: Data Evaluation/Data Usability
Data Evaluation
vs
Data Validation

## Slide 220: Data Evaluation/Data Useability
Benefits
Site-related vs artifact
Verification of reported concentrations
Elimination of data not representative of site conditions

## Slide 221: Evaluate data with respect to:
Analytical Method
Blank Samples
  10X Rule - common laboratory contaminants include acetone, 2-butanone, methylene chloride, toluene, phthalate esters
  5X rule – other constituents

## Slide 222: Interpreting blank sample results
Example: Methylene chloride was detected in the blank at 300 ug/l and in a groundwater sample at 2100 ug/l. Is it site-related or an artifact of the sampling/analysis process?
  Apply the 10X Rule: It is an artifact – methylene chloride would be considered to be site-related if the concentration in the groundwater sample was 10X greater than the concentration in the blank:
  300 ug/l X 10 = 3000 ug/l
  2100 ug/l < 3000 ug/l

## Slide 223: Interpreting blank sample results
Example: EDC was detected in the trip blank at 100 ug/l and in a groundwater sample at 1000 ug/l. Is it site-related or an artifact of the sampling/analysis process?
  Apply the 5X rule: Yes, it is site-related –EDC is present in the groundwater sample at a concentration that is 5X greater than the concentration in the blank:
  100 ug/l X 5 = 500 ug/l
  1000 ug/l > 500 ug/l

## Slide 224: Evaluate data with respect to:
Sample Quantitation Limits
  SQLs for ND results vs limiting RS
  If ND and SQL > RS, then not useful
  SQLs and calc of 95%UCL-AM
    SQL
    ½ SQL
  Matrix interferences
  One or more COC present at high concentrations

## Slide 225: Data evaluation section of risk assessment report should include:
Appropriateness of method and SQL*
TICs detected
  Few or many?
  Toxicity values available?
  Proprietary COC present?
  Breakdown products of concern?

## Slide 226: Data evaluation section of risk assessment report should include:
Codes and Qualifiers
  analytical laboratory vs data validators
  always refer to definitions provided
  almost all data is useable
  most qualifiers indicate uncertainty in concentration not identity of COC
    J – estimated value - useable
    R values - not useable due to quality control issues
    U – not detected
    RAGS-A Chapter 5 (EPA 1989)

## Slide 227: Use of historical data
Analytical methods and QA/QC are similar for both data sets
Types of COC - VOA vs Inorganic
Site history – soil disturbance or other?
Qualitative use of data
  Definitive vs visual
  SAP development

## Slide 228: Historical data
Historical data of unknown quality may not be used in determining AOIC
Analytical methods, sampling techniques, quantitation limits and QA/QC for the historical data shall be included
The elimination of any data set shall be fully justified in the risk assessment report

## Slide 229: MO-3

## Slide 230: MO-3
Always submit detailed workplan
All site-specific data must be documented
  Exposure data
  EF&T data
Greatly reduced EF and ED
  Taking land out of commerce
  Construction or maintenance worker scenarios
  RME
Complex modeling
  Inputs, outputs, supporting documentation
  Address in detail in workplan

## Slide 231: Workplans

## Slide 232: MO-2 and MO-3 Workplans
+/- MO-2 assessments
Required for all MO-3 assessments
Should be very detailed: COC, conceptual site model, toxicity data, all exposure and EF&T assumptions, methods, models, etc.
Approval of Workplans
Refer review to Toxicological Services Group

## Slide 233: RECAP Submittals Avoiding NODs

## Slide 234: Submittals: Key Points
Include all requirements listed for the Option
Include summary of previous RECAP assessments
Present all data/information necessary to reproduce calculations
  Id AOI and AOI dataset
  95% UCL-AM (dataset, ProUCL outputs, etc)
  site-specific SS or RS
  SS or RS not in Tables 1-3 (toxicity values, etc)
  Additivity adjustments and target organs

## Slide 235: Submittals: Key Points
  DF or DAF, VF, and PEF
  Modeling inputs/outputs
Present all data/information necessary to support conclusions
  Identify all applicable SS/RS and final LRS
  Present comparison of LRS and AOIC or CC
  Identify COC/areas/pathways > LRS
  Path forward

## Slide 236: Submittals: Key Points
Provide references (methods, input values, etc)
Provide supporting documentation for site-specific data/inputs
Use RECAP Submittal Forms (Appendix C)

## Slide 237: Frequent Deficiencies
Option being used not identified
Managing sites under Options they do not qualify for
Incomplete site characterization - horizontal and vertical extent not defined
AOI not properly identified
AOI not illustrated in a figure
Grouping multiple AOI into one large AOI
Dividing one AOI into multiple AOI
Notes: In April of this year, a much improved third draft was again released for public comment. This time the CAG received over 400 comments from organizations such as EPA, major oil companies, environmental consultants, and groups such as PIRI and LEAN. Most of these comments fell into three categories such as General, Typographical, and Technical. Most of the Technical comments concerned toxicological issues, surface water issues, and ecological risk assessment issues.
In September of this year, a revised final draft of the RECAP document was sent to the Legislative Oversight Committee and proposed for rulemaking. The Legislative Oversight Committee had 30 days to consider the proposed rule and hold a hearing on the rule to make comments and determine if the rule is acceptable. The Legislative Oversight Committee did not take any adverse action against the RECAP document and recommended the document be submitted to the Louisiana Register for publication.
With no adverse action taken by the Legislative Oversight Committee, the RECAP document could have been implemented as early as October 20th of this year. However, the LDEQ Administration decided to delay implementation until December 20th to allow time to get the document on the Internet, to provide internal training, to allow time to approve any outstanding CAPs, and to coincide with the 12/22/98 UST Deadline.

## Slide 238: Frequent Deficiencies
Failure to justify GW classification
Limiting SS or RS not identified
LRS not identified properly
SoilGW, Soilsat and/or Watersol not addressed
Additivity not addressed
Additivity addressed incorrectly
Use of incorrect SS or RS values (QC value)

## Slide 239: Frequent Deficiencies
Use of background levels not approved by Dept
Analyte list incomplete
RECAP forms not used
95%UCL-AM
  not calculated
  data set not provided
  data distribution not determined; wrong stats used
  calculations can’t be reproduced
  used for groundwater CC

## Slide 240: Frequent Deficiencies - TPH
Indicator compounds not addressed
Incorrect carbon ranges used
10,000 ppm ceiling value ignored
Additivity ignored
10,000 ppm adjusted for additivity

## Slide 241: Frequent Deficiencies
Data evaluation
    Not included
    Analytical data not included
    Elevated SQLs
    Omitting data sets without adequate documentation
No DOTD well survey (or outdated)
Notes: Currently, the RECAP document is available at the LDEQ web site.
The rulemaking process has been completed with the exception of publication in the Louisiana Register. The Department intends to publish the RECAP document in the December 20, 1998 edition of the Louisiana Register thereby making the document final rule.

## Slide 242: Frequent Deficiencies
Failure to identify input parameters
Calculations not presented
References not given
Toxicity Assessment
    Use of incorrect target organs
    Use of incorrect toxicity values
    References not given

## Slide 243: Remediation

## Slide 244: Remediation
Identification of area of remediation
   Use LRS for option being implemented
   Same principles as for id of AOI
Verification sampling
   sufficient number of samples for 95%UCL-AM
   samples representative of residual concentrations
Notes: I’d like to give you a brief overview of the RECAP Program and then Dr. Sutherlin will present a more detailed review.

## Slide 245: Remediation
Demonstration of compliance with LRS
  - Comparison of 95%UCL-AM with LRS
    If 95%UCL-AM > LRS  further action
    If 95%UCL-AM < LRS  NFA
  - 95%UCL-AM should include all verification samples within boundaries of the original area identified for remediation
Notes: I’d like to give you a brief overview of the RECAP Program and then Dr. Sutherlin will present a more detailed review.

## Slide 246: Remediation
Demonstration of compliance with LRS
  - Too few samples, high variability, or high number of ND, then 95%UCL-AM > max
  - Excavation/clean fill  volume weighted average for 95%UCL-AM
  - Nonpermanent structures/barriers - NO
    asphalt, concrete, etc
Notes: I’d like to give you a brief overview of the RECAP Program and then Dr. Sutherlin will present a more detailed review.